## Slide 1
ENGINEERING CORE
Essential Mathematics for Engineering
Core topic 4
Specification reference: 4.1, 4.2
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topic 4
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Essential Mathematics for Engineering
2
By the end of this lesson you should be able to:
1
Apply arithmetic, algebra and geometry to engineering problems.
2
Use trigonometry, graphs and basic calculus.
3
Calculate statistical measures.
4
Convert between decimal, binary and hexadecimal.
STARTER
A ladder 5 m long leans against a wall with its foot 3 m out. How high up the wall does it reach?

## Slide 3
ENGINEERING CORE · Core topic 4
The maths toolkit
Design and Development for Engineering and Manufacturing T Level · Essential Mathematics for Engineering
3
Area | What to be able to do
Arithmetic | Standard form, fractions, percentages, ratios, BIDMAS
Algebra | Rearrange equations; simultaneous and quadratic equations; indices; logarithms; sequences; matrices
Geometry | Areas of 2D shapes, volumes of 3D shapes
Calculus | Straight-line graphs y = mx + c; standard differentials and integrals; maximum and minimum
Trigonometry | Pythagoras, sine and cosine rules, radians, vectors
Statistics | Range, mean, median, mode, standard deviation, probability
Notes: Starter answer: Pythagoras, height = square root of (25 minus 9) = 4 m.

## Slide 4
ENGINEERING CORE · Core topic 4
Worked examples
Design and Development for Engineering and Manufacturing T Level · Essential Mathematics for Engineering
4
Standard form: 0.00045 m = 4.5 x 10 to the power -4 m.
Straight line: through (0, 2) with gradient 3 gives y = 3x + 2.
Volume of a cylinder: pi x r squared x h. For r = 0.1 m and h = 2 m, about 0.063 cubic metres.
Sine rule: a / sin A = b / sin B = c / sin C.
!
KEY IDEA
Always write the formula, substitute with units, then round sensibly. Most marks are lost in the working, not the maths.

## Slide 5
ENGINEERING CORE · Core topic 4
Number systems
Design and Development for Engineering and Manufacturing T Level · Essential Mathematics for Engineering
5
Decimal | Binary | Hexadecimal | Used for
10 | 1010 | A | Everyday counting
15 | 1111 | F | Binary: digital logic and PLC signals
255 | 11111111 | FF | Hex: memory addresses and machine codes

## Slide 6
ENGINEERING CORE · Core topic 4
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Essential Mathematics for Engineering
6
1
Write 0.0032 in standard form.
2
What is the gradient of y = 4x - 7?
3
Convert binary 1100 to decimal.
4
Find the mean of 12, 15, 18.
5
What is 180 degrees in radians?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 7
ENGINEERING CORE · Core topic 4
Answers
Design and Development for Engineering and Manufacturing T Level · Essential Mathematics for Engineering
7
1
Write 0.0032 in standard form.
3.2 x 10 to the power -3.
2
What is the gradient of y = 4x - 7?
4.
3
Convert binary 1100 to decimal.
12.
4
Find the mean of 12, 15, 18.
15.
5
What is 180 degrees in radians?
Pi radians.
Notes: Talk through any answers the class found difficult.

## Slide 8
ENGINEERING CORE · Core topic 4
Activity: Maths in the workshop
Design and Development for Engineering and Manufacturing T Level · Essential Mathematics for Engineering
8
30 minutes
Pairs
1
Work through the six engineering problems from your teacher (one per toolkit area).
2
Show the formula, substitution and units every time.
3
Check each answer with a partner.
4
Convert three sensor readings from binary to decimal and hex.
SUCCESS CRITERIA
Working shown clearly
Correct units
Conversions correct

## Slide 9
ENGINEERING CORE · Core topic 4
Exit ticket
1
Which area of maths do you find hardest?
2
Why do engineers use standard form?
3
Where might you meet hexadecimal in engineering?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 1
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/01-engineering-core-part1.md
Notes: Students answer on a sticky note or in the chat before leaving.