## Slide 1
ENGINEERING CORE
Forces, Motion and Energy
Core topics 5 and 7
Specification reference: 5.6, 7.1, 7.2
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topics 5 and 7
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
2
By the end of this lesson you should be able to:
1
Describe types of motion and calculate moments and torque.
2
Apply Newton's three laws of motion.
3
Calculate beam reactions for simply supported beams.
4
Calculate work, power and energy, and compare power sources.
STARTER
Why is it easier to open a door by pushing near the handle than near the hinge?

## Slide 3
ENGINEERING CORE · Core topics 5 and 7
Motion and moments
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
3
1
Types of motion
Rotary, linear, reciprocating, oscillating.
2
Moment
Force x perpendicular distance from the pivot (N m).
3
Equilibrium
Clockwise moments = anticlockwise moments, and forces balance.
4
Torque
The turning effect of a force about an axis.
Notes: Starter: the handle is further from the hinge, so the same force gives a bigger moment.

## Slide 4
ENGINEERING CORE · Core topics 5 and 7
Newton's laws of motion
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
4
1
First law
An object stays at rest or at constant velocity unless a resultant force acts.
2
Second law
Force = mass x acceleration (F = ma).
3
Third law
Every action has an equal and opposite reaction.

## Slide 5
ENGINEERING CORE · Core topics 5 and 7
Simply supported beams
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
5
A beam rests on two supports with loads applied.
Take moments about one support to find the other reaction.
Example: a 4 m beam with a 1,000 N load at its centre: each reaction is 500 N.
Shear force and bending moment diagrams show internal forces along the beam.
!
KEY IDEA
Check your answer: the two reactions must add up to the total load.

## Slide 6
ENGINEERING CORE · Core topics 5 and 7
Energy and power
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
6
Quantity | Formula
Work done | Force x distance moved (J)
Power | Work done / time (W)
Kinetic energy | Half x mass x velocity squared
Potential energy | Mass x g x height (g = 9.81 m/s squared)
Momentum | Mass x velocity; conserved in collisions
Power sources: mechanical, electrical and renewable, e.g. solar, hydro, wind, geothermal, fossil fuels, nuclear.

## Slide 7
ENGINEERING CORE · Core topics 5 and 7
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
7
1
A 20 N force acts 0.5 m from a pivot. What is the moment?
2
What force accelerates a 2 kg mass at 3 m/s squared?
3
State Newton's third law.
4
What is the kinetic energy of 4 kg moving at 3 m/s?
5
A motor does 600 J of work in 10 s. What is its power?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 8
ENGINEERING CORE · Core topics 5 and 7
Answers
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
8
1
A 20 N force acts 0.5 m from a pivot. What is the moment?
10 N m.
2
What force accelerates a 2 kg mass at 3 m/s squared?
6 N.
3
State Newton's third law.
Every action has an equal and opposite reaction.
4
What is the kinetic energy of 4 kg moving at 3 m/s?
18 J.
5
A motor does 600 J of work in 10 s. What is its power?
60 W.
Notes: Talk through any answers the class found difficult.

## Slide 9
ENGINEERING CORE · Core topics 5 and 7
Activity: Beam challenge
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
9
30 minutes
Pairs
1
A 6 m beam carries 2 kN at 2 m from the left support.
2
Calculate both support reactions.
3
Sketch the shear force diagram.
4
Check your reactions add up to the load.
SUCCESS CRITERIA
Moments taken correctly
Reactions of 1.33 kN (left) and 0.67 kN (right)
Diagram labelled
Notes: Answer: taking moments about the left support, right reaction = 2 x 2 / 6 = 0.67 kN; left reaction = 1.33 kN.

## Slide 10
ENGINEERING CORE · Core topics 5 and 7
Exit ticket
1
Give an everyday example of Newton's first law.
2
Why does a flywheel store energy?
3
Compare two power sources for a remote farm.
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 1
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/01-engineering-core-part1.md
Notes: Students answer on a sticky note or in the chat before leaving.