## Slide 1
ENGINEERING CORE
Fluid Dynamics and Thermodynamics
Core topic 5
Specification reference: 5.7, 5.8
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topic 5
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
2
By the end of this lesson you should be able to:
1
Explain hydrostatic pressure, viscosity and Bernoulli's principle.
2
Describe laminar and turbulent flow and aerodynamic forces.
3
Describe heat transfer and sensible and latent heat.
4
Apply Boyle's law, Charles' law and the general gas equation.
STARTER
Why do your ears hurt at the bottom of a swimming pool but not at the top?

## Slide 3
ENGINEERING CORE · Core topic 5
Fluids at rest and in motion
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
3
1
Hydrostatic pressure
Pressure = density x g x depth. It rises with depth.
2
Viscosity
A fluid's resistance to flow: honey is more viscous than water.
3
Bernoulli's principle
Where a fluid speeds up, its pressure drops.
4
Flow types
Laminar (smooth layers) and turbulent (chaotic), with vortices and separation points.

## Slide 4
ENGINEERING CORE · Core topic 5
Aerodynamics
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
4
1
Lift
Upward force from pressure difference across a wing.
2
Drag
Resistance opposing motion through air.
3
Thrust
Force that drives an object forward.
Notes: Liquids are nearly incompressible; air is compressible, which is a key difference between liquid flow and aerodynamics.

## Slide 5
ENGINEERING CORE · Core topic 5
Heat
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
5
Heat transfer
Conduction: through solids
Convection: by moving fluids
Radiation: by electromagnetic waves
Open and closed systems
Types of heat
Sensible heat changes temperature
Latent heat changes state at constant temperature
Expansivity: materials expand when heated

## Slide 6
ENGINEERING CORE · Core topic 5
The gas laws
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
6
Law | Relationship | Held constant
Boyle's law | p1 V1 = p2 V2 | Temperature
Charles' law | V1 / T1 = V2 / T2 | Pressure
General gas equation | p1 V1 / T1 = p2 V2 / T2 | Mass of gas
Characteristic gas equation | pV = mRT | R for the gas
Temperatures in gas laws must be in kelvin: K = degrees C + 273.

## Slide 7
ENGINEERING CORE · Core topic 5
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
7
1
What happens to pressure as depth increases?
2
State Bernoulli's principle.
3
Which heat changes state without changing temperature?
4
A gas at 100 kPa is squeezed from 2 L to 1 L at constant temperature. New pressure?
5
Convert 27 degrees C to kelvin.
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 8
ENGINEERING CORE · Core topic 5
Answers
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
8
1
What happens to pressure as depth increases?
It increases.
2
State Bernoulli's principle.
Where a fluid's speed increases, its pressure decreases.
3
Which heat changes state without changing temperature?
Latent heat.
4
A gas at 100 kPa is squeezed from 2 L to 1 L at constant temperature. New pressure?
200 kPa.
5
Convert 27 degrees C to kelvin.
300 K.
Notes: Talk through any answers the class found difficult.

## Slide 9
ENGINEERING CORE · Core topic 5
Activity: Gas law problems
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
9
25 minutes
Pairs
1
Solve the four gas law problems from your teacher.
2
State which law applies and what is held constant.
3
Convert all temperatures to kelvin.
4
Explain one real engineering application of each law.
SUCCESS CRITERIA
Correct law chosen
Kelvin used
Answers with units

## Slide 10
ENGINEERING CORE · Core topic 5
Exit ticket
1
Why must gas law temperatures be in kelvin?
2
Give one example of convection in engineering.
3
Why does a car spoiler create downforce?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 1
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/01-engineering-core-part1.md
Notes: Students answer on a sticky note or in the chat before leaving.