## Slide 1
ENGINEERING CORE
Materials: Chemistry, Properties and Structures
Core topics 5 and 6
Specification reference: 5.5, 6.1, 6.2
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topics 5 and 6
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
2
By the end of this lesson you should be able to:
1
Describe atomic structure, bonding and chemical behaviour of materials.
2
Distinguish physical and mechanical properties and calculate density.
3
Describe the main families of engineering materials.
4
Describe smart materials and their uses.
STARTER
Why is a kettle's body made of metal or plastic, but its handle always plastic?

## Slide 3
ENGINEERING CORE · Core topics 5 and 6
Chemistry for engineers
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
3
1
Atoms
Nucleus of protons and neutrons, surrounded by electrons; valence electrons form bonds.
2
Bonding
Metallic, covalent, ionic and van der Waals bonds.
3
Electrical chemistry
Cells, capacity, internal resistance and electrolysis.
4
Reactions
Metals react with acids and alkalis: used in etching and surface finishing.

## Slide 4
ENGINEERING CORE · Core topics 5 and 6
Properties of materials
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
4
Physical
Density = mass / volume
Melting point
Thermal and electrical conductivity
Thermal expansivity, corrosion resistance
Weldability, recyclability
Mechanical
Strength: tensile, compressive, shear, torsion
Hardness and toughness
Brittleness and ductility
Elasticity and plasticity
Malleability

## Slide 5
ENGINEERING CORE · Core topics 5 and 6
Families of materials
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
5
Family | Examples
Ferrous metals | Cast iron, carbon steels, stainless steel
Non-ferrous metals | Aluminium, copper, brass, zinc
Thermoplastics / thermosets | ABS, acrylic / epoxy resin, melamine
Elastomers | Rubber, neoprene
Composites | GRP, carbon fibre (CRP), MDF
Ceramics | Silicon carbide, glass

## Slide 6
ENGINEERING CORE · Core topics 5 and 6
Smart materials
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
6
1
Shape memory alloys
Return to a set shape when heated.
2
Quantum tunnelling composite
Conducts when squeezed.
3
Thermochromic / photochromic
Change colour with heat / light.
4
Piezoelectric crystals
Produce a voltage when stressed.

## Slide 7
ENGINEERING CORE · Core topics 5 and 6
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
7
1
A block has mass 2.7 kg and volume 0.001 cubic metres. What is its density?
2
What is the difference between hardness and toughness?
3
Is brass ferrous or non-ferrous?
4
Which smart material produces a voltage under stress?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 8
ENGINEERING CORE · Core topics 5 and 6
Answers
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
8
1
A block has mass 2.7 kg and volume 0.001 cubic metres. What is its density?
2,700 kg per cubic metre (aluminium).
2
What is the difference between hardness and toughness?
Hardness resists scratching and wear; toughness resists fracture from impact.
3
Is brass ferrous or non-ferrous?
Non-ferrous.
4
Which smart material produces a voltage under stress?
A piezoelectric crystal.
Notes: Talk through any answers the class found difficult.

## Slide 9
ENGINEERING CORE · Core topics 5 and 6
Activity: Material detective
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
9
25 minutes
Small groups
1
Examine the material samples from your teacher.
2
Identify each family and one likely material.
3
Measure mass and volume to calculate density for two samples.
4
Match each sample to a suitable product and justify it by properties.
SUCCESS CRITERIA
Families correct
Density calculated with units
Justifications use property names

## Slide 10
ENGINEERING CORE · Core topics 5 and 6
Exit ticket
1
Why are thermosets used for plug sockets?
2
What is ductility?
3
Name one use of a shape memory alloy.
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 1
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/01-engineering-core-part1.md
Notes: Students answer on a sticky note or in the chat before leaving.