## Slide 1
ENGINEERING CORE
Material Processing, Treatment, Failure and Testing
Core topic 6
Specification reference: 6.3, 6.4, 6.5, 6.6
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topic 6
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
2
By the end of this lesson you should be able to:
1
Explain how processing changes material properties.
2
Describe heat treatments and surface treatments.
3
Explain causes of failure: corrosion, fatigue and creep.
4
Interpret tensile test results and calculate stress, strain and Young's modulus.
STARTER
Bend a paperclip back and forth until it snaps. What just happened to the metal?

## Slide 3
ENGINEERING CORE · Core topic 6
Heat and surface treatments
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
3
Treatment | Effect
Case hardening | Hard outer surface, tough core
Quench hardening / tempering | Harden steel, then reduce brittleness
Normalising / annealing | Refine grain / soften and relieve stress
Precipitation hardening | Strengthens some alloys, e.g. aluminium
Painting, plastic coating, galvanising | Barrier or sacrificial protection against corrosion
Notes: Processing also changes properties: rolling, forging, welding, casting, sintering, hot and cold working, curing thermosets.

## Slide 4
ENGINEERING CORE · Core topic 6
Why materials fail
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
4
1
Corrosion
Oxidation, chemical attack or stress corrosion eats material away.
2
Fatigue
Repeated loading below the breaking stress causes cracks: the paperclip.
3
Creep
Slow deformation under constant load, often at high temperature, in three stages.
4
Prevention
Coatings, galvanising, sacrificial anodes, good design.

## Slide 5
ENGINEERING CORE · Core topic 6
Tensile testing
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
5
Quantity | Formula or meaning
Stress | Force / cross-sectional area (N per square metre, Pa)
Strain | Extension / original length (no units)
Young's modulus | Stress / strain, in the elastic region
Hooke's law | Extension is proportional to load up to the limit of proportionality
Ultimate tensile strength | The maximum stress before necking and fracture
Other tests: visual, toughness (impact), hardness, corrosion, wear, fatigue (Wohler), conductivity.

## Slide 6
ENGINEERING CORE · Core topic 6
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
6
1
What is fatigue failure?
2
A 1,000 N force acts on 0.0001 square metres. What is the stress?
3
A 2 m bar stretches 1 mm. What is the strain?
4
Why temper after quench hardening?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 7
ENGINEERING CORE · Core topic 6
Answers
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
7
1
What is fatigue failure?
Failure caused by repeated cyclic loading below the ultimate strength.
2
A 1,000 N force acts on 0.0001 square metres. What is the stress?
10,000,000 Pa (10 MPa).
3
A 2 m bar stretches 1 mm. What is the strain?
0.0005.
4
Why temper after quench hardening?
To reduce brittleness.
Notes: Talk through any answers the class found difficult.

## Slide 8
ENGINEERING CORE · Core topic 6
Activity: Read a load-extension graph
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
8
25 minutes
Pairs
1
Use the tensile test data from your teacher.
2
Mark the elastic limit, UTS and fracture point on the graph.
3
Calculate stress, strain and Young's modulus in the elastic region.
4
Identify the material from its modulus.
SUCCESS CRITERIA
Key points labelled
Calculations with units
Sensible identification

## Slide 9
ENGINEERING CORE · Core topic 6
Exit ticket
1
Why is galvanising called sacrificial protection?
2
Where would creep be a concern?
3
What does Young's modulus tell you?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 1
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/01-engineering-core-part1.md
Notes: Students answer on a sticky note or in the chat before leaving.