## Slide 1
ENGINEERING CORE
Mechatronics, PLCs, Hydraulics and Pneumatics
Core topic 9
Specification reference: 9.1, 9.2, 9.3
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topic 9
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Mechatronics, PLCs, Hydraulics and Pneumatics
2
By the end of this lesson you should be able to:
1
Identify the mechanical, electronic and drive components of a mechatronic system.
2
Compare PLC types and explain how a PLC operates.
3
Compare hydraulic and pneumatic systems and their components.
STARTER
A car wash moves along a car, sprays, brushes and dries it. List every sensor and motor you think it needs.

## Slide 3
ENGINEERING CORE · Core topic 9
Components of a mechatronic system
Design and Development for Engineering and Manufacturing T Level · Mechatronics, PLCs, Hydraulics and Pneumatics
3
1
Mechanical
Gears, cams, linkages, levers, pulleys.
2
Electronic
Sensors, transducers, microprocessors, microcontrollers, actuators.
3
Drives
Standard electric motors, servo motors, stepper motors.
Notes: Mechatronics integrates mechanical and electronic systems into one functioning system. Servo motors give precise position control with feedback; stepper motors move in fixed steps.

## Slide 4
ENGINEERING CORE · Core topic 9
Programmable logic controllers (PLCs)
Design and Development for Engineering and Manufacturing T Level · Mechatronics, PLCs, Hydraulics and Pneumatics
4
1
Types
Unitary, unitary with modular features, and modular.
2
Operation
Condition sensor signals, run the program, drive outputs.
3
Function
Process blocks, motor driver ICs, interface devices.
4
Applications
Robotic arms, conveyors, packaging, SCADA, remote units, animatronics.
Notes: Compared with dedicated ICs or computers, PLCs are rugged, easily reprogrammed and built for industrial I/O, but cost more than a simple dedicated circuit.

## Slide 5
ENGINEERING CORE · Core topic 9
Hydraulics and pneumatics
Design and Development for Engineering and Manufacturing T Level · Mechatronics, PLCs, Hydraulics and Pneumatics
5
Hydraulics (oil)
Nearly incompressible fluid
Very high forces, precise control
Risk of leaks and fire from oil
e.g. excavators, presses
Pneumatics (air)
Compressible, so springy
Fast, clean and cheap
Lower forces, less precise
e.g. pick-and-place, doors on buses
Notes: Components: valves, pumps, actuators, cylinders, compressors. Students should recognise them on schematic diagrams.

## Slide 6
ENGINEERING CORE · Core topic 9
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Mechatronics, PLCs, Hydraulics and Pneumatics
6
1
Name two electronic components in a mechatronic system.
2
What is the difference between a unitary and a modular PLC?
3
Which system uses a nearly incompressible fluid?
4
Which motor moves in fixed steps?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 7
ENGINEERING CORE · Core topic 9
Answers
Design and Development for Engineering and Manufacturing T Level · Mechatronics, PLCs, Hydraulics and Pneumatics
7
1
Name two electronic components in a mechatronic system.
Any two of: sensors, transducers, microprocessors, microcontrollers, actuators.
2
What is the difference between a unitary and a modular PLC?
A unitary PLC is a single fixed unit; a modular PLC is built from plug-in modules.
3
Which system uses a nearly incompressible fluid?
Hydraulics.
4
Which motor moves in fixed steps?
A stepper motor.
Notes: Talk through any answers the class found difficult.

## Slide 8
ENGINEERING CORE · Core topic 9
Activity: Design a sorting system
Design and Development for Engineering and Manufacturing T Level · Mechatronics, PLCs, Hydraulics and Pneumatics
8
30 minutes
Small groups
1
A conveyor must push large boxes onto a second belt and let small boxes pass.
2
Choose sensors, a PLC type and an actuator.
3
Decide between pneumatic and hydraulic actuation and justify it.
4
Sketch a block diagram of the system.
SUCCESS CRITERIA
Input, process and output all present
Actuator choice justified
Diagram is clear

## Slide 9
ENGINEERING CORE · Core topic 9
Exit ticket
1
Why are PLCs popular in factories?
2
When would you choose pneumatics?
3
What does a transducer do?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 2
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/02-engineering-core-part2.md
Notes: Students answer on a sticky note or in the chat before leaving.