## Slide 1
ENGINEERING CORE
Control Systems, Sensors and Actuators
Core topic 10
Specification reference: 10.1, 10.2
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topic 10
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Control Systems, Sensors and Actuators
2
By the end of this lesson you should be able to:
1
Describe inputs, processes and outputs, including logic gates.
2
Compare open and closed loop control and explain feedback.
3
Explain steady-state error, damping and signal types.
4
Describe sensors and actuators used in automation.
STARTER
A toaster runs for a set time. An oven holds 180 degrees. Which one 'knows' what is happening? How?

## Slide 3
ENGINEERING CORE · Core topic 10
Parts of a control system
Design and Development for Engineering and Manufacturing T Level · Control Systems, Sensors and Actuators
3
1
Input
Sensors measuring pressure, flow, temperature, speed or position.
2
Process
Logic gates (AND, OR, NOT), timers, comparators, counters, latches.
3
Output
Motors, valves, heaters, lamps.
4
Feedback
The output is measured and fed back to the input.

## Slide 4
ENGINEERING CORE · Core topic 10
Open and closed loop
Design and Development for Engineering and Manufacturing T Level · Control Systems, Sensors and Actuators
4
Open loop
No feedback
Simple and cheap
Cannot correct errors
e.g. a toaster on a timer
Closed loop
Feedback via a summing point compares output to the set point
Corrects errors automatically
Can overshoot (under-damped) or be slow (over-damped)
e.g. an oven thermostat, cruise control
Notes: Steady-state error is the difference that remains between the set point and the output once the system settles. A transfer function describes the output/input relationship of a block.

## Slide 5
ENGINEERING CORE · Core topic 10
Signals and modulation
Design and Development for Engineering and Manufacturing T Level · Control Systems, Sensors and Actuators
5
Term | Meaning
Analogue signal | Continuously variable value
Digital signal | Discrete on or off levels
Pulse width modulation | Varies the on-time of pulses to control power, e.g. motor speed
Pulse amplitude modulation | Varies the height of pulses to carry information

## Slide 6
ENGINEERING CORE · Core topic 10
Sensors and actuators in automation
Design and Development for Engineering and Manufacturing T Level · Control Systems, Sensors and Actuators
6
1
Types
Analogue or digital; active (needs power) or passive.
2
Examples
Switches, proximity sensors, lasers, vision systems.
3
Connections
Hard-wired or wireless; suitable power sources.
4
Uses
Positioning, measuring, lifting and moving objects.

## Slide 7
ENGINEERING CORE · Core topic 10
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Control Systems, Sensors and Actuators
7
1
What does a closed loop system have that an open loop one doesn't?
2
Which logic gate outputs 1 only when both inputs are 1?
3
What is steady-state error?
4
How does PWM control motor speed?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 8
ENGINEERING CORE · Core topic 10
Answers
Design and Development for Engineering and Manufacturing T Level · Control Systems, Sensors and Actuators
8
1
What does a closed loop system have that an open loop one doesn't?
Feedback.
2
Which logic gate outputs 1 only when both inputs are 1?
AND.
3
What is steady-state error?
The difference left between the set point and the output once settled.
4
How does PWM control motor speed?
By varying how long the power is on in each pulse.
Notes: Talk through any answers the class found difficult.

## Slide 9
ENGINEERING CORE · Core topic 10
Activity: System diagram
Design and Development for Engineering and Manufacturing T Level · Control Systems, Sensors and Actuators
9
25 minutes
Pairs
1
Draw a closed loop system diagram for a greenhouse that controls temperature and watering.
2
Show two inputs, two outputs, the controller and feedback paths.
3
Label the summing points and set points.
4
Explain what would happen if it were under-damped.
SUCCESS CRITERIA
Multiple inputs and outputs shown
Feedback correctly drawn
Damping explained

## Slide 10
ENGINEERING CORE · Core topic 10
Exit ticket
1
Give an example of a passive sensor.
2
Why might a system overshoot?
3
Name one process block used in control systems.
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 2
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/02-engineering-core-part2.md
Notes: Students answer on a sticky note or in the chat before leaving.