## Slide 1
MECHANICAL ENGINEERING
Simple Machines and Mechanical Calculations
Mechanical: Knowledge criteria
Specification reference: 1.5, 1.6, 1.13
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
2
By the end of this lesson you should be able to:
1
Describe gears, pulleys, levers, linkages, cams and ratchets.
2
Calculate gear ratios for simple and compound gear trains.
3
Calculate mechanical advantage, velocity ratio and efficiency.
4
Apply stress, strain and beam calculations to design.
STARTER
A bike's pedal gear has 48 teeth and the rear gear has 16. How many times does the wheel turn for each pedal turn?

## Slide 3
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Simple machines
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
3
1
Gears
Spur, helical, bevel, worm, rack and pinion.
2
Levers
Class 1 (seesaw), class 2 (wheelbarrow), class 3 (tweezers).
3
Linkages
Reverse motion, parallel motion, bell crank, crank and slider.
4
Cams
Circular, eccentric and snail (drop) cams turn rotary into reciprocating motion.
5
Pulleys and ratchets
Change force direction; allow motion one way only.
Notes: Each machine changes the magnitude, direction or type of motion.

## Slide 4
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Gear trains
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
4
Gear ratio = teeth on driven gear / teeth on driver gear.
Output speed = input speed / gear ratio.
Compound train: multiply the ratios of each pair.
Starter: 16 / 48 = 1/3, so the wheel turns 3 times per pedal turn.
!
KEY IDEA
A ratio above 1 slows the output and increases torque. Below 1 speeds it up and reduces torque.

## Slide 5
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Machine performance
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
5
Quantity | Formula
Mechanical advantage (MA) | Load / effort
Velocity ratio (VR) | Distance moved by effort / distance moved by load
Efficiency | MA / VR x 100%
Work | Force x distance
Power | Work / time

## Slide 6
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Force calculations
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
6
Quantity | Formula
Stress | Force / area
Strain | Extension / original length
Young's modulus | Stress / strain
Beam reactions | Take moments about a support; reactions sum to the total load
Material quantity and cost | Area or volume x unit cost, plus manufacturing cost
Notes: Beams can be simply supported or cantilevered; learners calculate reactions, shear force and bending moment.

## Slide 7
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
7
1
A 20-tooth driver meshes with a 60-tooth driven gear. Gear ratio?
2
If the driver turns at 900 rpm, what is the output speed?
3
A pulley lifts 400 N with 100 N effort. MA?
4
If VR is 5 and MA is 4, what is the efficiency?
5
Which lever class is a wheelbarrow?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 8
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Answers
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
8
1
A 20-tooth driver meshes with a 60-tooth driven gear. Gear ratio?
3:1.
2
If the driver turns at 900 rpm, what is the output speed?
300 rpm.
3
A pulley lifts 400 N with 100 N effort. MA?
4.
4
If VR is 5 and MA is 4, what is the efficiency?
80%.
5
Which lever class is a wheelbarrow?
Class 2.
Notes: Talk through any answers the class found difficult.

## Slide 9
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Activity: Design a winch
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
9
35 minutes
Pairs
1
A winch must lift 2,000 N using a 250 N effort.
2
Design a compound gear train to achieve it.
3
Calculate MA, VR and efficiency assuming 80% efficiency.
4
Suggest where a ratchet is needed and why.
SUCCESS CRITERIA
Gear ratio calculated correctly
Efficiency accounted for
Ratchet placement justified

## Slide 10
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Exit ticket
1
Why can't efficiency ever reach 100%?
2
Which gear type changes the axis by 90 degrees?
3
What does a cam follower do?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Knowledge Criteria
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/02-occupational-specialism/01-knowledge-criteria.md
Notes: Students answer on a sticky note or in the chat before leaving.