## Slide 1
MECHANICAL ENGINEERING
Quality, Testing and Measurement
Mechanical: Knowledge criteria
Specification reference: 1.15, 1.17, 1.18, 1.19
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
2
By the end of this lesson you should be able to:
1
Distinguish assignable from random causes of error.
2
Compare quality assurance and quality control, and sampling with 100% inspection.
3
Compare non-destructive and destructive testing methods.
4
Choose measurement equipment and analyse measurement data statistically.
STARTER
Two operators measure the same part and get different results. List every reason why.

## Slide 3
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Causes of error
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
3
Assignable (systematic)
Faulty calibration
Tool wear
Observer bias
Human error
Can be found and fixed
Random
Ambient conditions
Temperature and humidity
Instrument uncertainty
Reduced, not eliminated
Notes: Quality assurance: procedures, calibration, process capability monitoring, preventative maintenance. Quality control: testing and inspection. Production quantity decides between sampling and 100% inspection.

## Slide 4
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Testing methods
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
4
Type | Method | Detects
Non-destructive | Visual, measurement, go/no-go gauges | Surface and dimensional faults
Non-destructive | Ultrasonic, X-radiography | Internal flaws
Non-destructive | Penetrant, magnetic particle | Surface cracks
Destructive | Tensile, hardness | Strength and hardness
Destructive | Impact (Izod, Charpy), macro examination | Toughness and internal structure

## Slide 5
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Measurement equipment
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
5
Equipment | Use
Rules, protractors | Basic length and angle
Vernier and digital callipers | Inside, outside and depth
Micrometers (outside, inside, depth) | Precise small dimensions
Gauges (go/no-go, slip, plug) | Quick pass or fail checks; reference lengths
DTI, CMM, laser scanning | Run-out, complex 3D geometry
Digital stress/strain machines | Mechanical properties
Analyse results with mean, range and standard deviation to judge whether parts are in tolerance.

## Slide 6
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
6
1
Is tool wear an assignable or random cause?
2
Which test finds internal flaws without damaging the part?
3
What does a Charpy test measure?
4
What does a go/no-go gauge do?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 7
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Answers
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
7
1
Is tool wear an assignable or random cause?
Assignable.
2
Which test finds internal flaws without damaging the part?
Ultrasonic testing or X-radiography.
3
What does a Charpy test measure?
Toughness (impact energy absorbed).
4
What does a go/no-go gauge do?
Quickly checks whether a feature is within limits.
Notes: Talk through any answers the class found difficult.

## Slide 8
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Activity: Is the batch in tolerance?
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
8
30 minutes
Pairs, practical
1
Measure ten parts with a micrometer.
2
Calculate the mean, range and standard deviation.
3
Compare with the drawing tolerance.
4
Decide whether the process needs adjusting and suggest a cause.
SUCCESS CRITERIA
Measurements recorded correctly
Statistics accurate
Decision justified

## Slide 9
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Exit ticket
1
When would you use destructive testing?
2
Why calibrate measuring equipment?
3
What does a large standard deviation tell you?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Knowledge Criteria
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/02-occupational-specialism/01-knowledge-criteria.md
Notes: Students answer on a sticky note or in the chat before leaving.