## Slide 1
ENGINEERING CORE
Engineering Drawings, Dimensions and Tolerancing
Core topic 3
Specification reference: 3.1, 3.2
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topic 3
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
2
By the end of this lesson you should be able to:
1
Choose drawing types for a purpose and audience.
2
Interpret title blocks, line types, abbreviations and symbols.
3
Interpret dimensions and GD&T symbols.
4
Calculate tolerances, limits and fits.
STARTER
A shaft is drawn as 20 mm diameter. Could a real shaft ever be exactly 20.000 mm? What does that mean for making it?

## Slide 3
ENGINEERING CORE · Core topic 3
Drawing types
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
3
1
Sketches and isometric
Quick ideas and 3D views for discussion.
2
Orthographic projection
Accurate 2D views for manufacture.
3
Exploded views
Show how parts assemble.
4
CAD models
Accurate 3D models that can be simulated.
5
Diagrams
Block diagrams, flowcharts, circuit diagrams and schematics.
Notes: Drawings follow BS EN 8888 (technical product documentation) and BS 3939 (graphical symbols).

## Slide 4
ENGINEERING CORE · Core topic 3
Common abbreviations
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
4
Abbreviation | Meaning | Abbreviation | Meaning
AF | Across flats | CSK | Countersink
CL | Centre line | HEX | Hexagon
DIA | Diameter | PCD | Pitch circle diameter
DWG | Drawing | THD | Thread
MTL | Material | UCUT | Undercut
CHAM | Chamfer | SQ / R | Square / radius

## Slide 5
ENGINEERING CORE · Core topic 3
Tolerances, limits and fits
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
5
Tolerance: the total allowed variation in a dimension.
Limits: the largest and smallest acceptable sizes.
Example: 20 mm plus or minus 0.1 mm gives limits of 19.9 mm and 20.1 mm, a tolerance of 0.2 mm.
Fits: clearance (always a gap), interference (always tight), transition (either).
!
KEY IDEA
Tighter tolerances cost more to make. Only specify what the function really needs.

## Slide 6
ENGINEERING CORE · Core topic 3
Geometric tolerancing (GD&T)
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
6
1
Datum
A reference surface or feature to measure from.
2
Parallelism
A surface stays parallel to a datum.
3
Perpendicularity
A surface stays at 90 degrees to a datum.
4
Concentricity
Circular features share a centre.
5
Straightness
A line or edge stays straight.

## Slide 7
ENGINEERING CORE · Core topic 3
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
7
1
What does PCD stand for?
2
A hole is 12 mm plus or minus 0.05 mm. What are its limits?
3
Which fit always has a gap?
4
Which drawing type is best for showing assembly?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 8
ENGINEERING CORE · Core topic 3
Answers
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
8
1
What does PCD stand for?
Pitch circle diameter.
2
A hole is 12 mm plus or minus 0.05 mm. What are its limits?
11.95 mm and 12.05 mm.
3
Which fit always has a gap?
A clearance fit.
4
Which drawing type is best for showing assembly?
An exploded view.
Notes: Talk through any answers the class found difficult.

## Slide 9
ENGINEERING CORE · Core topic 3
Activity: Read the drawing
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
9
25 minutes
Pairs
1
Study the orthographic drawing from your teacher.
2
List every abbreviation and symbol and what it means.
3
Calculate the limits for three toleranced dimensions.
4
Identify the fit between the shaft and the hole.
SUCCESS CRITERIA
All symbols correctly explained
Limits calculated accurately
Fit type justified

## Slide 10
ENGINEERING CORE · Core topic 3
Exit ticket
1
Who would use an isometric sketch rather than an orthographic drawing?
2
Why do tighter tolerances cost more?
3
What is a datum?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 1
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/01-engineering-core-part1.md
Notes: Students answer on a sticky note or in the chat before leaving.