## Slide 1
ENGINEERING CORE
Units, Measurement and Scientific Method
Core topic 5
Specification reference: 5.1, 5.2, 5.3, 5.4
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topic 5
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
2
By the end of this lesson you should be able to:
1
Use SI and imperial units and convert between them.
2
Distinguish vectors and scalars, and polar and Cartesian coordinates.
3
Apply the scientific method to testing.
4
Choose measurement equipment and explain accuracy, precision and calibration.
STARTER
Is 'the car travelled 30 miles' a speed, a velocity or a distance? What would make it a velocity?

## Slide 3
ENGINEERING CORE · Core topic 5
Units
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
3
Quantity | SI unit | Note
Length, mass, time | m, kg, s | Base units
Force | newton (N) | Derived: kg m/s squared
Pressure | pascal (Pa) | N per square metre
Torque | newton metre (N m) | Force x distance
Density | kg per cubic metre | Mass / volume
Prefixes | tera to pico | k = 1,000; m = 0.001; micro = 0.000001
Imperial units: foot, inch, yard, ounce, gallon. 1 inch = 25.4 mm.

## Slide 4
ENGINEERING CORE · Core topic 5
Vectors and coordinates
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
4
Scalars and vectors
Scalar: size only, e.g. distance, speed
Vector: size and direction, e.g. displacement, velocity, acceleration
Coordinates
Cartesian: (x, y)
Polar: (r, angle)
x = r cos angle, y = r sin angle
r = square root of (x squared + y squared)

## Slide 5
ENGINEERING CORE · Core topic 5
The scientific method
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
5
1
Observe
Notice something.
2
Question
Ask why.
3
Hypothesise
Suggest an explanation.
4
Predict
Predict or simulate a result.
5
Test
Run a fair test.
6
Conclude
Accept or reject, then iterate.
Judge results on accuracy, reliability, precision and whether they can be replicated.

## Slide 6
ENGINEERING CORE · Core topic 5
Measurement equipment
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
6
Equipment | Measures | Typical resolution
Steel rule | Lengths | 0.5 mm
Vernier / digital calliper | Inside, outside and depth | 0.02 / 0.01 mm
Micrometer | Small diameters and thicknesses | 0.01 mm
Dial test indicator | Small variations, run-out | 0.01 mm
CMM | Complex 3D geometry | Microns
Notes: Principles: precision (repeatability), accuracy (closeness to the true value), uncertainty, resolution, calibration and tolerance.

## Slide 7
ENGINEERING CORE · Core topic 5
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
7
1
Is velocity a scalar or a vector?
2
Convert 3 inches to millimetres.
3
What is the difference between accuracy and precision?
4
Why calibrate equipment?
5
Which tool would you use to measure a 6 mm shaft diameter most precisely?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 8
ENGINEERING CORE · Core topic 5
Answers
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
8
1
Is velocity a scalar or a vector?
A vector.
2
Convert 3 inches to millimetres.
76.2 mm.
3
What is the difference between accuracy and precision?
Accuracy is closeness to the true value; precision is repeatability.
4
Why calibrate equipment?
So its readings match a known standard.
5
Which tool would you use to measure a 6 mm shaft diameter most precisely?
A micrometer.
Notes: Talk through any answers the class found difficult.

## Slide 9
ENGINEERING CORE · Core topic 5
Activity: Measure and compare
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
9
30 minutes
Pairs, practical
1
Measure the same three components with a rule, a calliper and a micrometer.
2
Record five readings each.
3
Calculate the mean and range for each tool.
4
Explain which tool is most precise and why.
SUCCESS CRITERIA
Readings recorded with units
Mean and range correct
Conclusion uses accuracy and precision correctly

## Slide 10
ENGINEERING CORE · Core topic 5
Exit ticket
1
Give a derived SI unit and what it measures.
2
Why repeat measurements?
3
What is resolution?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 1
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/01-engineering-core-part1.md
Notes: Students answer on a sticky note or in the chat before leaving.