## Slide 1
ENGINEERING CORE
Electrical and Electronic Principles
Core topic 8
Specification reference: 8.1
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topic 8
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Electrical and Electronic Principles
2
By the end of this lesson you should be able to:
1
Explain charge, current, voltage, resistance and power.
2
Apply Ohm's law and Kirchhoff's laws to series and parallel circuits.
3
Describe AC and DC, protection systems and semiconductors.
4
Compare analogue and digital signals.
STARTER
Why does a fuse blow instead of the wires in your house catching fire?

## Slide 3
ENGINEERING CORE · Core topic 8
Key quantities
Design and Development for Engineering and Manufacturing T Level · Electrical and Electronic Principles
3
Quantity | Unit | Formula
Current (I) | amp (A) | Charge / time
Voltage (V) | volt (V) | V = I x R (Ohm's law)
Resistance (R) | ohm | R = V / I
Power (P) | watt (W) | P = V x I

## Slide 4
ENGINEERING CORE · Core topic 8
Series and parallel
Design and Development for Engineering and Manufacturing T Level · Electrical and Electronic Principles
4
Series
Same current through every component
Voltages add up to the supply
Total R = R1 + R2 + ...
Parallel
Same voltage across each branch
Currents add up to the total
1 / R total = 1 / R1 + 1 / R2 + ...
Notes: Kirchhoff's current law: current into a junction equals current out. Voltage law: voltages around a loop sum to zero.

## Slide 5
ENGINEERING CORE · Core topic 8
AC, protection and components
Design and Development for Engineering and Manufacturing T Level · Electrical and Electronic Principles
5
1
AC and DC
AC reverses direction (mains); DC flows one way (batteries). Phasor diagrams show AC phase.
2
Protection
Fuses, RCDs and lightning arrestors; differential and transformer protection.
3
Capacitors and inductors
Store energy in electric and magnetic fields; time constants in DC circuits.
4
Semiconductors
Diodes let current flow one way; transistors switch and amplify.

## Slide 6
ENGINEERING CORE · Core topic 8
Signals
Design and Development for Engineering and Manufacturing T Level · Electrical and Electronic Principles
6
Analogue
Continuously variable
e.g. a thermistor's voltage
Affected by noise
Digital
Discrete levels: on or off
e.g. a limit switch
Robust, easy to process
Fan in / fan out limits how many gates connect

## Slide 7
ENGINEERING CORE · Core topic 8
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Electrical and Electronic Principles
7
1
A 12 V supply drives 2 A. What is the resistance?
2
Two 10 ohm resistors in series: total resistance?
3
Two 10 ohm resistors in parallel: total resistance?
4
What does an RCD do?
5
What does a diode do?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 8
ENGINEERING CORE · Core topic 8
Answers
Design and Development for Engineering and Manufacturing T Level · Electrical and Electronic Principles
8
1
A 12 V supply drives 2 A. What is the resistance?
6 ohms.
2
Two 10 ohm resistors in series: total resistance?
20 ohms.
3
Two 10 ohm resistors in parallel: total resistance?
5 ohms.
4
What does an RCD do?
Cuts the supply when it detects a current imbalance (leakage).
5
What does a diode do?
Lets current flow in one direction only.
Notes: Talk through any answers the class found difficult.

## Slide 9
ENGINEERING CORE · Core topic 8
Activity: Circuit calculations
Design and Development for Engineering and Manufacturing T Level · Electrical and Electronic Principles
9
30 minutes
Pairs, with breadboards if available
1
Build (or sketch) a series and a parallel circuit with two resistors.
2
Predict currents and voltages using Ohm's law.
3
Measure them with a multimeter.
4
Explain any differences between prediction and measurement.
SUCCESS CRITERIA
Predictions calculated correctly
Meter used safely
Differences explained (tolerance, meter resistance)

## Slide 10
ENGINEERING CORE · Core topic 8
Exit ticket
1
Why are house circuits wired in parallel?
2
What is the power of a 230 V, 5 A heater?
3
Give one advantage of digital signals.
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 1
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/01-engineering-core-part1.md
Notes: Students answer on a sticky note or in the chat before leaving.