## Slide 1
ENGINEERING CORE
Engineering Drawings, Dimensions and Tolerancing
Core topic 3
Specification reference: 3.1, 3.2
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topic 3
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
2
By the end of this lesson you should be able to:
1
Choose drawing types for a purpose and audience.
2
Interpret title blocks, line types, abbreviations and symbols.
3
Interpret dimensions and GD&T symbols.
4
Calculate tolerances, limits and fits.
STARTER
A shaft is drawn as 20 mm diameter. Could a real shaft ever be exactly 20.000 mm? What does that mean for making it?

## Slide 3
ENGINEERING CORE · Core topic 3
Drawing types
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
3
Engineers choose a drawing type to suit its purpose and audience.
Freehand sketches capture ideas quickly. Isometric drawings show an object in 3D at a fixed angle, easy for anyone to understand. Orthographic projection shows accurate 2D views (front, side and plan) with dimensions, used for manufacture. Exploded views show how parts fit together. CAD models are accurate 3D models that can be tested virtually. Block diagrams, flowcharts, circuit diagrams and schematics show systems.
Drawings follow standards such as BS EN 8888 for technical drawings and BS 3939 for graphical symbols.
e.g.
EXAMPLE
A customer sees an isometric rendering; the machinist works from an orthographic drawing; the assembly team uses an exploded view.

## Slide 4
ENGINEERING CORE · Core topic 3
Drawing types
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
4
1
Sketches and isometric
Quick ideas and 3D views for discussion.
2
Orthographic projection
Accurate 2D views for manufacture.
3
Exploded views
Show how parts assemble.
4
CAD models
Accurate 3D models that can be simulated.
5
Diagrams
Block diagrams, flowcharts, circuit diagrams and schematics.
Notes: Drawings follow BS EN 8888 (technical product documentation) and BS 3939 (graphical symbols).

## Slide 5
ENGINEERING CORE · Core topic 3
Quick check: Drawing types
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
5
1
Which drawing type is used for manufacture?
2
What does an exploded view show?
3
Which standard covers technical drawings?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Orthographic projection.
2. How parts assemble.
3. BS EN 8888.

## Slide 6
ENGINEERING CORE · Core topic 3
Common abbreviations
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
6
Abbreviation | Meaning | Abbreviation | Meaning
AF | Across flats | CSK | Countersink
CL | Centre line | HEX | Hexagon
DIA | Diameter | PCD | Pitch circle diameter
DWG | Drawing | THD | Thread
MTL | Material | UCUT | Undercut
CHAM | Chamfer | SQ / R | Square / radius

## Slide 7
ENGINEERING CORE · Core topic 3
Tolerances, limits and fits
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
7
No part can be made to an exact size, so drawings state how much variation is acceptable.
The tolerance is the total allowed variation. The limits are the largest and smallest acceptable sizes. A dimension of 20 mm plus or minus 0.1 mm has limits of 19.9 mm and 20.1 mm and a tolerance of 0.2 mm.
Fits describe how two parts go together. A clearance fit always leaves a gap, so parts move freely. An interference fit is always tight, so parts must be pressed together. A transition fit could be either.
Tighter tolerances cost more, so specify only what the function needs.
e.g.
EXAMPLE
A shaft is 25.00 to 25.02 mm and its hole 25.05 to 25.08 mm. The smallest gap is 0.03 mm, so it's a clearance fit and the shaft always turns freely.

## Slide 8
ENGINEERING CORE · Core topic 3
Tolerances, limits and fits
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
8
Tolerance: the total allowed variation in a dimension.
Limits: the largest and smallest acceptable sizes.
Example: 20 mm plus or minus 0.1 mm gives limits of 19.9 mm and 20.1 mm, a tolerance of 0.2 mm.
Fits: clearance (always a gap), interference (always tight), transition (either).
!
KEY IDEA
Tighter tolerances cost more to make. Only specify what the function really needs.

## Slide 9
ENGINEERING CORE · Core topic 3
Quick check: Tolerances, limits and fits
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
9
1
A dimension is 50 mm plus or minus 0.2 mm. What are the limits?
2
Which fit always needs pressing together?
3
Why not make every tolerance tight?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. 49.8 mm and 50.2 mm.
2. An interference fit.
3. Tighter tolerances cost more to make.

## Slide 10
ENGINEERING CORE · Core topic 3
Geometric tolerancing (GD&T)
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
10
Size tolerances aren't always enough: a hole can be the right size but in the wrong place or at the wrong angle. Geometric dimensioning and tolerancing (GD&T) controls form, orientation and position.
A datum is a reference surface or feature everything is measured from. Parallelism keeps a surface parallel to a datum. Perpendicularity keeps it at 90 degrees. Concentricity keeps circular features on the same centre. Straightness keeps a line or edge straight.
Each has a standard symbol in a feature control frame on the drawing.
e.g.
EXAMPLE
A bearing bore must be concentric with the shaft centre line within 0.02 mm, or the shaft will wobble and wear the bearing.

## Slide 11
ENGINEERING CORE · Core topic 3
Geometric tolerancing (GD&T)
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
11
1
Datum
A reference surface or feature to measure from.
2
Parallelism
A surface stays parallel to a datum.
3
Perpendicularity
A surface stays at 90 degrees to a datum.
4
Concentricity
Circular features share a centre.
5
Straightness
A line or edge stays straight.

## Slide 12
ENGINEERING CORE · Core topic 3
Quick check: Geometric tolerancing (GD&T)
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
12
1
What is a datum?
2
What does concentricity control?
3
Why isn't size tolerance always enough?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. A reference feature that other features are measured from.
2. That circular features share the same centre.
3. A feature can be the right size but wrongly positioned or angled.

## Slide 13
ENGINEERING CORE · Core topic 3
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
13
1
What does PCD stand for?
2
A hole is 12 mm plus or minus 0.05 mm. What are its limits?
3
Which fit always has a gap?
4
Which drawing type is best for showing assembly?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 14
ENGINEERING CORE · Core topic 3
Answers
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
14
1
What does PCD stand for?
Pitch circle diameter.
2
A hole is 12 mm plus or minus 0.05 mm. What are its limits?
11.95 mm and 12.05 mm.
3
Which fit always has a gap?
A clearance fit.
4
Which drawing type is best for showing assembly?
An exploded view.
Notes: Talk through any answers the class found difficult.

## Slide 15
ENGINEERING CORE · Core topic 3
Activity: Read the drawing
Design and Development for Engineering and Manufacturing T Level · Engineering Drawings, Dimensions and Tolerancing
15
25 minutes
Pairs
1
Study the orthographic drawing from your teacher.
2
List every abbreviation and symbol and what it means.
3
Calculate the limits for three toleranced dimensions.
4
Identify the fit between the shaft and the hole.
SUCCESS CRITERIA
All symbols correctly explained
Limits calculated accurately
Fit type justified

## Slide 16
ENGINEERING CORE · Core topic 3
Exit ticket
1
Who would use an isometric sketch rather than an orthographic drawing?
2
Why do tighter tolerances cost more?
3
What is a datum?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 1
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/01-engineering-core-part1.md
Notes: Students answer on a sticky note or in the chat before leaving.