## Slide 1
ENGINEERING CORE
Units, Measurement and Scientific Method
Core topic 5
Specification reference: 5.1, 5.2, 5.3, 5.4
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topic 5
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
2
By the end of this lesson you should be able to:
1
Use SI and imperial units and convert between them.
2
Distinguish vectors and scalars, and polar and Cartesian coordinates.
3
Apply the scientific method to testing.
4
Choose measurement equipment and explain accuracy, precision and calibration.
STARTER
Is 'the car travelled 30 miles' a speed, a velocity or a distance? What would make it a velocity?

## Slide 3
ENGINEERING CORE · Core topic 5
Units
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
3
SI base units include the metre (length), kilogram (mass) and second (time). Derived units combine them: the newton (N) for force, the pascal (Pa, newtons per square metre) for pressure, the newton metre for torque, metres per second for velocity and kilograms per cubic metre for density.
Prefixes scale units from tera (10 to the power 12) to pico (10 to the power -12). Common ones: kilo (1,000), mega (1,000,000), milli (0.001) and micro (0.000001).
Some industries still use imperial units, such as the inch (25.4 mm) and foot, so conversions matter.
e.g.
EXAMPLE
A pressure of 2.5 MPa is 2,500,000 Pa. A 2 inch pipe is 50.8 mm.

## Slide 4
ENGINEERING CORE · Core topic 5
Units
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
4
Quantity | SI unit | Note
Length, mass, time | m, kg, s | Base units
Force | newton (N) | Derived: kg m/s squared
Pressure | pascal (Pa) | N per square metre
Torque | newton metre (N m) | Force x distance
Density | kg per cubic metre | Mass / volume
Prefixes | tera to pico | k = 1,000; m = 0.001; micro = 0.000001
Imperial units: foot, inch, yard, ounce, gallon. 1 inch = 25.4 mm.

## Slide 5
ENGINEERING CORE · Core topic 5
Quick check: Units
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
5
1
What is the SI unit of force?
2
How many pascals in 1 kPa?
3
Convert 4 inches to millimetres.
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. The newton (N).
2. 1,000.
3. 101.6 mm.

## Slide 6
ENGINEERING CORE · Core topic 5
Vectors and coordinates
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
6
A scalar has size only, such as distance, speed or mass. A vector has size and direction, such as displacement, velocity, acceleration or force. Walking 5 km is a distance; walking 5 km north is a displacement.
Positions can be described with Cartesian coordinates (x, y) or polar coordinates (a distance r and an angle). To convert polar to Cartesian: x = r cos angle, y = r sin angle. To convert back: r = square root of (x squared + y squared).
CNC machines and robots use both systems to position tools.
e.g.
EXAMPLE
A robot arm reaches 0.5 m at 30 degrees: x = 0.5 cos 30 = 0.43 m, y = 0.5 sin 30 = 0.25 m.

## Slide 7
ENGINEERING CORE · Core topic 5
Vectors and coordinates
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
7
Scalars and vectors
Scalar: size only, e.g. distance, speed
Vector: size and direction, e.g. displacement, velocity, acceleration
Coordinates
Cartesian: (x, y)
Polar: (r, angle)
x = r cos angle, y = r sin angle
r = square root of (x squared + y squared)

## Slide 8
ENGINEERING CORE · Core topic 5
Quick check: Vectors and coordinates
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
8
1
Is speed a scalar or a vector?
2
How do you convert polar to Cartesian x?
3
Give an example of a vector.
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. A scalar.
2. x = r cos angle.
3. E.g. velocity, displacement, force.

## Slide 9
ENGINEERING CORE · Core topic 5
The scientific method
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
9
Engineers test ideas scientifically rather than guessing.
Observe something, ask a question, form a hypothesis (a testable explanation), make a prediction or run a simulation, carry out a fair test, and draw a conclusion. Then iterate: refine the hypothesis and test again.
Judge results by accuracy (how close to the true value), reliability (consistent results), precision (how close repeated readings are to each other) and replication (whether others get the same result).
e.g.
EXAMPLE
Hypothesis: a thicker bracket won't crack under vibration. Test three thicknesses on a vibration rig, repeat each test, and compare with the prediction.

## Slide 10
ENGINEERING CORE · Core topic 5
The scientific method
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
10
1
Observe
Notice something.
2
Question
Ask why.
3
Hypothesise
Suggest an explanation.
4
Predict
Predict or simulate a result.
5
Test
Run a fair test.
6
Conclude
Accept or reject, then iterate.
Judge results on accuracy, reliability, precision and whether they can be replicated.

## Slide 11
ENGINEERING CORE · Core topic 5
Quick check: The scientific method
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
11
1
What is a hypothesis?
2
What is precision?
3
Why repeat tests?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. A testable explanation.
2. How close repeated readings are to each other.
3. To check results are reliable.

## Slide 12
ENGINEERING CORE · Core topic 5
Measurement equipment
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
12
Choose measuring equipment by the accuracy you need.
A steel rule measures to about 0.5 mm. Vernier and digital callipers measure inside, outside and depth dimensions to about 0.02 mm. Micrometers measure small diameters and thicknesses to 0.01 mm or better. Dial test indicators show small variations such as run-out. Coordinate measuring machines (CMMs) measure complex 3D shapes to microns.
Key principles: resolution (the smallest change it can show), accuracy, precision, uncertainty, calibration against a known standard, and tolerance.
e.g.
EXAMPLE
Checking a 12 mm shaft toleranced to plus or minus 0.01 mm needs a micrometer: a calliper isn't precise enough.

## Slide 13
ENGINEERING CORE · Core topic 5
Measurement equipment
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
13
Equipment | Measures | Typical resolution
Steel rule | Lengths | 0.5 mm
Vernier / digital calliper | Inside, outside and depth | 0.02 / 0.01 mm
Micrometer | Small diameters and thicknesses | 0.01 mm
Dial test indicator | Small variations, run-out | 0.01 mm
CMM | Complex 3D geometry | Microns
Notes: Principles: precision (repeatability), accuracy (closeness to the true value), uncertainty, resolution, calibration and tolerance.

## Slide 14
ENGINEERING CORE · Core topic 5
Quick check: Measurement equipment
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
14
1
Which tool measures small diameters most precisely?
2
What is resolution?
3
Why calibrate instruments?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. A micrometer.
2. The smallest change an instrument can show.
3. So readings match a known standard.

## Slide 15
ENGINEERING CORE · Core topic 5
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
15
1
Is velocity a scalar or a vector?
2
Convert 3 inches to millimetres.
3
What is the difference between accuracy and precision?
4
Why calibrate equipment?
5
Which tool would you use to measure a 6 mm shaft diameter most precisely?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 16
ENGINEERING CORE · Core topic 5
Answers
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
16
1
Is velocity a scalar or a vector?
A vector.
2
Convert 3 inches to millimetres.
76.2 mm.
3
What is the difference between accuracy and precision?
Accuracy is closeness to the true value; precision is repeatability.
4
Why calibrate equipment?
So its readings match a known standard.
5
Which tool would you use to measure a 6 mm shaft diameter most precisely?
A micrometer.
Notes: Talk through any answers the class found difficult.

## Slide 17
ENGINEERING CORE · Core topic 5
Activity: Measure and compare
Design and Development for Engineering and Manufacturing T Level · Units, Measurement and Scientific Method
17
30 minutes
Pairs, practical
1
Measure the same three components with a rule, a calliper and a micrometer.
2
Record five readings each.
3
Calculate the mean and range for each tool.
4
Explain which tool is most precise and why.
SUCCESS CRITERIA
Readings recorded with units
Mean and range correct
Conclusion uses accuracy and precision correctly

## Slide 18
ENGINEERING CORE · Core topic 5
Exit ticket
1
Give a derived SI unit and what it measures.
2
Why repeat measurements?
3
What is resolution?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 1
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/01-engineering-core-part1.md
Notes: Students answer on a sticky note or in the chat before leaving.