## Slide 1
ENGINEERING CORE
Risk Assessment and Hazardous Contexts
Core topic 12
Specification reference: 12.4, 12.5
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topic 12
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Risk Assessment and Hazardous Contexts
2
By the end of this lesson you should be able to:
1
Identify hazards using HAZOP and HAZID.
2
Evaluate risk by likelihood, severity and number of people affected.
3
Apply the hierarchy of control.
4
Describe safety considerations in specific engineering contexts.
STARTER
Name as many hazards as you can in a machine workshop in 60 seconds.

## Slide 3
ENGINEERING CORE · Core topic 12
Stages of risk assessment
Design and Development for Engineering and Manufacturing T Level · Risk Assessment and Hazardous Contexts
3
Risk assessment has three core stages.
Identify hazards: anything that could cause harm, such as machinery, stored energy, tools, electricity, harmful substances and the environment. Methods include HAZOP (a structured study of a process) and HAZID (hazard identification workshops).
Evaluate the risk: how likely harm is, how severe it would be and how many people could be affected.
Implement control measures using the hierarchy of control, then record and review them.
e.g.
EXAMPLE
A pressurised air receiver: hazard (stored energy), risk (explosion injuring several people), control (pressure relief valve, regular inspection, guarding).

## Slide 4
ENGINEERING CORE · Core topic 12
Stages of risk assessment
Design and Development for Engineering and Manufacturing T Level · Risk Assessment and Hazardous Contexts
4
1
Identify hazards
HAZOP, HAZID, inspection.
2
Evaluate risk
Likelihood, severity, number of people affected.
3
Control
Apply the hierarchy of control.
4
Record and review
Document and check it still works.
Notes: Engineering hazards: equipment, stored energy, tools, electricity, harmful substances and gases, environments.

## Slide 5
ENGINEERING CORE · Core topic 12
Quick check: Stages of risk assessment
Design and Development for Engineering and Manufacturing T Level · Risk Assessment and Hazardous Contexts
5
1
What is a hazard?
2
Name the three factors in evaluating risk.
3
What is HAZOP?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Anything that could cause harm.
2. Likelihood, severity and number of people affected.
3. A structured study of a process to find hazards.

## Slide 6
ENGINEERING CORE · Core topic 12
The hierarchy of control
Design and Development for Engineering and Manufacturing T Level · Risk Assessment and Hazardous Contexts
6
Controls are chosen from the top of the hierarchy down, because higher controls are more effective.
Eliminate the hazard completely. Reduce it or substitute something less hazardous. Isolate people from it. Use engineering controls such as guards, interlocks and extraction. Use administrative controls: training, safe systems of work, permits and signs. Finally, provide PPE such as eye and ear protection, safety shoes, gauntlets and helmets.
PPE is the last resort because it only protects the wearer and depends on being worn correctly.
e.g.
EXAMPLE
Noisy machine: replace it with a quieter one (substitute), enclose it (engineering), limit exposure time (administrative), then provide ear defenders (PPE).

## Slide 7
ENGINEERING CORE · Core topic 12
The hierarchy of control
Design and Development for Engineering and Manufacturing T Level · Risk Assessment and Hazardous Contexts
7
1
Eliminate
Remove the hazard.
2
Reduce / substitute
Use something less hazardous.
3
Isolate
Separate people from the hazard.
4
Engineering controls
Guards, extraction, interlocks.
5
Administration
Training, safe systems of work.
6
PPE
The last resort.

## Slide 8
ENGINEERING CORE · Core topic 12
Quick check: The hierarchy of control
Design and Development for Engineering and Manufacturing T Level · Risk Assessment and Hazardous Contexts
8
1
What is the top level of the hierarchy?
2
Give an example of an engineering control.
3
Why is PPE the last resort?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Elimination.
2. E.g. guards, interlocks, extraction.
3. It only protects the wearer and relies on correct use.

## Slide 9
ENGINEERING CORE · Core topic 12
Specific engineering contexts
Design and Development for Engineering and Manufacturing T Level · Risk Assessment and Hazardous Contexts
9
Some work needs extra precautions.
Moving parts need guarding and isolation. Lock out tag out (LOTO) means switching off and physically locking energy sources before work, so nobody can restart the machine. Confined spaces risk suffocation and need oxygen checks, a permit to work and a rescue plan. Chemicals need COSHH assessments, ventilation and fire precautions. Electrical testing and high-voltage work need safe isolation, permits and competent people, and awareness of stored energy.
e.g.
EXAMPLE
Before clearing a jam in a conveyor, the fitter isolates the power, fits their own padlock and tag, and tests that it won't start.

## Slide 10
ENGINEERING CORE · Core topic 12
Specific engineering contexts
Design and Development for Engineering and Manufacturing T Level · Risk Assessment and Hazardous Contexts
10
Context | Key considerations
Moving parts | Guarding, isolation, lock out tag out (LOTO)
Confined spaces | Asphyxiation, oxygen levels, permit to work, rescue plan
Chemicals | COSHH, ventilation, fire and explosion risk
Electrical testing and high voltage | Isolation, permits, stored energy, competent persons
Maintenance | Safe isolation, heat, manual handling

## Slide 11
ENGINEERING CORE · Core topic 12
Quick check: Specific engineering contexts
Design and Development for Engineering and Manufacturing T Level · Risk Assessment and Hazardous Contexts
11
1
What is LOTO?
2
What is a permit to work?
3
Why are confined spaces dangerous?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Locking and tagging energy sources off before work.
2. Written authorisation with conditions for high-risk work.
3. E.g. lack of oxygen, toxic gases, difficult escape.

## Slide 12
ENGINEERING CORE · Core topic 12
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Risk Assessment and Hazardous Contexts
12
1
What is the first level of the hierarchy of control?
2
Why is PPE the last resort?
3
What is LOTO?
4
What does a permit to work control?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 13
ENGINEERING CORE · Core topic 12
Answers
Design and Development for Engineering and Manufacturing T Level · Risk Assessment and Hazardous Contexts
13
1
What is the first level of the hierarchy of control?
Elimination.
2
Why is PPE the last resort?
It only protects the wearer and relies on it being worn correctly.
3
What is LOTO?
Lock out tag out: isolating and locking energy sources before work.
4
What does a permit to work control?
Authorisation and conditions for high-risk work.
Notes: Talk through any answers the class found difficult.

## Slide 14
ENGINEERING CORE · Core topic 12
Activity: Risk assess the lathe
Design and Development for Engineering and Manufacturing T Level · Risk Assessment and Hazardous Contexts
14
30 minutes
Small groups
1
Risk assess using a centre lathe in the workshop.
2
Identify at least five hazards.
3
Score likelihood and severity for each.
4
Choose controls from as high up the hierarchy as possible.
SUCCESS CRITERIA
Hazards are specific
Scores justified
PPE is not the only control

## Slide 15
ENGINEERING CORE · Core topic 12
Exit ticket
1
Give an example of an engineering control.
2
What is HAZOP used for?
3
Why are confined spaces dangerous?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 2
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/02-engineering-core-part2.md
Notes: Students answer on a sticky note or in the chat before leaving.