## Slide 1
ENGINEERING CORE
Design Principles and Manufacturing Approaches
Core topic 1
Specification reference: 1.1, 1.3
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topic 1
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Design Principles and Manufacturing Approaches
2
By the end of this lesson you should be able to:
1
Describe the main types of manufacturing process.
2
Compare linear, iterative and other approaches to design, including the 6Rs.
3
Relate scale of manufacture to infrastructure and automation.
4
Explain the role of CAM, quality assurance and quality control.
STARTER
Pick up any object near you. How do you think it was made? Could it be made a different way?

## Slide 3
ENGINEERING CORE · Core topic 1
Types of manufacturing process
Design and Development for Engineering and Manufacturing T Level · Design Principles and Manufacturing Approaches
3
Manufacturing processes are grouped by how they change material.
Wasting removes material to leave the shape you want: cutting, drilling, turning and milling. It's accurate but creates waste. Forming bends or presses material without removing any. Shaping and casting pour or push material into a mould. Joining connects parts by welding, brazing, fixings or adhesives. Finishing protects or improves the surface. Additive manufacturing, such as 3D printing, builds a part layer by layer, so complex shapes are possible with little waste.
The process chosen affects cost, quantity, accuracy, strength and appearance.
e.g.
EXAMPLE
A steel bracket could be milled from a solid block (wasting), laser cut then bent (forming), or 3D printed in metal (additive). Bending sheet is cheapest in volume.

## Slide 4
ENGINEERING CORE · Core topic 1
Types of manufacturing process
Design and Development for Engineering and Manufacturing T Level · Design Principles and Manufacturing Approaches
4
1
Wasting
Removing material: cutting, drilling, milling, turning.
2
Forming and shaping
Bending or pressing material, or moulding it into shape.
3
Casting
Pouring molten material into a mould.
4
Joining
Welding, brazing, fixings, adhesives.
5
Finishing
Coatings and surface treatments.
6
Additive
Building layer by layer, e.g. 3D printing.

## Slide 5
ENGINEERING CORE · Core topic 1
Quick check: Types of manufacturing process
Design and Development for Engineering and Manufacturing T Level · Design Principles and Manufacturing Approaches
5
1
Which process type removes material?
2
Why is additive manufacturing good for complex shapes?
3
Name two joining methods.
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Wasting.
2. It builds parts layer by layer.
3. E.g. welding, brazing, fixings, adhesives.

## Slide 6
ENGINEERING CORE · Core topic 1
Approaches to design
Design and Development for Engineering and Manufacturing T Level · Design Principles and Manufacturing Approaches
6
Linear design moves through fixed stages in order: brief, research, specification, ideas, development, manufacture and evaluation. It's easy to manage but slow to react to problems.
Iterative design cycles through design, test, evaluate and improve, repeatedly. Test results feed each new version, so problems are found early.
Other approaches include inclusive and user-centred design (designing around real users), design for manufacture and assembly (making parts easy to make and fit together), and sustainable design, guided by the 6Rs: reduce, refuse, rethink, repair, reuse and recycle.
Anthropometric data, body measurements, makes products fit people.
e.g.
EXAMPLE
Designing a drill handle: anthropometric data sets the grip size; three 3D-printed iterations are tested with users before the final design.

## Slide 7
ENGINEERING CORE · Core topic 1
Approaches to design
Design and Development for Engineering and Manufacturing T Level · Design Principles and Manufacturing Approaches
7
Linear and iterative
Linear: brief, research, specification, ideas, develop, make, evaluate, in order
Iterative: design, test, evaluate, improve, repeat
Testing results feed the next iteration
Other approaches
Inclusive and user-centred design
Design for manufacture and assembly
Sustainable design and the 6Rs: reduce, refuse, rethink, repair, reuse, recycle
Notes: Fitness for purpose covers functional and environmental requirements. User requirements come from design briefs and specifications. Students should be able to interpret anthropometric (ergonomic) data.

## Slide 8
ENGINEERING CORE · Core topic 1
Quick check: Approaches to design
Design and Development for Engineering and Manufacturing T Level · Design Principles and Manufacturing Approaches
8
1
What is the key difference between linear and iterative design?
2
Name three of the 6Rs.
3
What is anthropometric data?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Iterative repeats test and improve cycles; linear goes through stages once.
2. Any three: reduce, refuse, rethink, repair, reuse, recycle.
3. Measurements of the human body, used for ergonomic design.

## Slide 9
ENGINEERING CORE · Core topic 1
Scale of manufacture
Design and Development for Engineering and Manufacturing T Level · Design Principles and Manufacturing Approaches
9
How many products are made shapes how they're made.
One-off: a single bespoke item, made by skilled workers or with computer-aided manufacture (CAM). Batch: a set quantity, then the equipment is changed over for the next product. Mass: very large numbers on dedicated, highly automated production lines. Continuous: production runs non-stop, such as steel sheet or chemicals.
Higher volumes justify more automation and investment in tooling, lowering the cost of each item. Factories can be laid out by function, by product, as a matrix, or in cells.
e.g.
EXAMPLE
A racing car wing is one-off; a run of 500 brackets is batch; car door handles are mass produced; petrol is refined continuously.

## Slide 10
ENGINEERING CORE · Core topic 1
Scale of manufacture
Design and Development for Engineering and Manufacturing T Level · Design Principles and Manufacturing Approaches
10
Scale | Example | Typical automation
One-off | A bespoke racing car part | Manual or CAM
Batch | A run of 500 brackets | CAM with changeovers
Mass | Car door handles | Largely automated production lines
Continuous | Steel sheet, chemicals | Fully automated, runs non-stop

## Slide 11
ENGINEERING CORE · Core topic 1
Quick check: Scale of manufacture
Design and Development for Engineering and Manufacturing T Level · Design Principles and Manufacturing Approaches
11
1
Which scale suits bespoke items?
2
Why does mass production use more automation?
3
Give an example of continuous production.
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. One-off.
2. High volumes justify the investment and lower unit cost.
3. E.g. steel sheet, chemicals, petrol.

## Slide 12
ENGINEERING CORE · Core topic 1
Infrastructure and control
Design and Development for Engineering and Manufacturing T Level · Design Principles and Manufacturing Approaches
12
1
Infrastructure
Functional, product and matrix layouts; cellular manufacture; production lines.
2
Automation levels
Manual, computer-aided manufacture (CAM), fully automated, robotic.
3
Control
Performance monitoring, quality assurance and quality control.

## Slide 13
ENGINEERING CORE · Core topic 1
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Design Principles and Manufacturing Approaches
13
1
Which type of process removes material?
2
Name three of the 6Rs.
3
Which scale of manufacture suits steel sheet?
4
What does CAM stand for?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 14
ENGINEERING CORE · Core topic 1
Answers
Design and Development for Engineering and Manufacturing T Level · Design Principles and Manufacturing Approaches
14
1
Which type of process removes material?
Wasting.
2
Name three of the 6Rs.
Any three of: reduce, refuse, rethink, repair, reuse, recycle.
3
Which scale of manufacture suits steel sheet?
Continuous.
4
What does CAM stand for?
Computer-aided manufacture.
Notes: Talk through any answers the class found difficult.

## Slide 15
ENGINEERING CORE · Core topic 1
Activity: Make it at scale
Design and Development for Engineering and Manufacturing T Level · Design Principles and Manufacturing Approaches
15
25 minutes
Small groups
1
Your product is a bike bottle cage.
2
Suggest how it would be made as a one-off, a batch of 200, and mass produced.
3
Choose manufacturing processes and automation levels for each.
4
Apply two of the 6Rs to improve its sustainability.
SUCCESS CRITERIA
Processes match the scale
Automation choices justified
6Rs applied specifically

## Slide 16
ENGINEERING CORE · Core topic 1
Exit ticket
1
Why is iterative design often better than linear?
2
Give one advantage of cellular manufacture.
3
What is the difference between quality assurance and quality control?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 1
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/01-engineering-core-part1.md
Notes: Students answer on a sticky note or in the chat before leaving.