## Slide 1
ENGINEERING CORE
Forces, Motion and Energy
Core topics 5 and 7
Specification reference: 5.6, 7.1, 7.2
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topics 5 and 7
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
2
By the end of this lesson you should be able to:
1
Describe types of motion and calculate moments and torque.
2
Apply Newton's three laws of motion.
3
Calculate beam reactions for simply supported beams.
4
Calculate work, power and energy, and compare power sources.
STARTER
Why is it easier to open a door by pushing near the handle than near the hinge?

## Slide 3
ENGINEERING CORE · Core topics 5 and 7
Motion and moments
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
3
Motion can be rotary (turning), linear (in a straight line), reciprocating (back and forth in a line) or oscillating (swinging back and forth in an arc).
A moment is the turning effect of a force: moment = force x perpendicular distance from the pivot, measured in newton metres. Torque is the turning effect about an axis, such as on a bolt or shaft.
An object is in equilibrium when the forces balance and the clockwise moments equal the anticlockwise moments. Engineers use this to find unknown forces.
e.g.
EXAMPLE
A 40 N force on a spanner 0.25 m from the bolt gives 40 x 0.25 = 10 N m of torque. A longer spanner gives more torque for the same force.

## Slide 4
ENGINEERING CORE · Core topics 5 and 7
Motion and moments
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
4
1
Types of motion
Rotary, linear, reciprocating, oscillating.
2
Moment
Force x perpendicular distance from the pivot (N m).
3
Equilibrium
Clockwise moments = anticlockwise moments, and forces balance.
4
Torque
The turning effect of a force about an axis.
Notes: Starter: the handle is further from the hinge, so the same force gives a bigger moment.

## Slide 5
ENGINEERING CORE · Core topics 5 and 7
Quick check: Motion and moments
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
5
1
What is the formula for a moment?
2
What motion does a piston make?
3
What is equilibrium?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Force x perpendicular distance.
2. Reciprocating.
3. Forces balance and clockwise moments equal anticlockwise moments.

## Slide 6
ENGINEERING CORE · Core topics 5 and 7
Newton's laws of motion
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
6
Newton's first law: an object stays at rest, or keeps moving at a constant velocity, unless a resultant (unbalanced) force acts on it.
Newton's second law: force = mass x acceleration (F = ma). A bigger force, or a smaller mass, gives a bigger acceleration.
Newton's third law: when one object pushes on another, the second pushes back with an equal and opposite force.
These laws explain everything from a car braking to a rocket launching.
e.g.
EXAMPLE
A 1,200 kg car accelerating at 2 m/s squared needs a resultant force of 1,200 x 2 = 2,400 N.

## Slide 7
ENGINEERING CORE · Core topics 5 and 7
Newton's laws of motion
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
7
1
First law
An object stays at rest or at constant velocity unless a resultant force acts.
2
Second law
Force = mass x acceleration (F = ma).
3
Third law
Every action has an equal and opposite reaction.

## Slide 8
ENGINEERING CORE · Core topics 5 and 7
Quick check: Newton's laws of motion
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
8
1
State Newton's second law as a formula.
2
What force accelerates 50 kg at 3 m/s squared?
3
Which law explains recoil when firing?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. F = ma.
2. 150 N.
3. Newton's third law.

## Slide 9
ENGINEERING CORE · Core topics 5 and 7
Simply supported beams
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
9
A simply supported beam rests on two supports and carries loads.
To find the support reactions, take moments about one support: the moment of the load about that support equals the moment of the other reaction about it. Then the reactions must add up to the total load.
Shear force diagrams show the internal sliding forces along the beam; bending moment diagrams show where it bends most. The maximum bending moment tells designers where the beam is most likely to fail.
e.g.
EXAMPLE
A 6 m beam with 3 kN at 2 m from the left support: right reaction = 3 x 2 / 6 = 1 kN; left reaction = 3 - 1 = 2 kN.

## Slide 10
ENGINEERING CORE · Core topics 5 and 7
Simply supported beams
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
10
A beam rests on two supports with loads applied.
Take moments about one support to find the other reaction.
Example: a 4 m beam with a 1,000 N load at its centre: each reaction is 500 N.
Shear force and bending moment diagrams show internal forces along the beam.
!
KEY IDEA
Check your answer: the two reactions must add up to the total load.

## Slide 11
ENGINEERING CORE · Core topics 5 and 7
Quick check: Simply supported beams
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
11
1
How do you find a support reaction?
2
What must the reactions add up to?
3
What does a bending moment diagram show?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Take moments about the other support.
2. The total load.
3. Where and how much the beam bends.

## Slide 12
ENGINEERING CORE · Core topics 5 and 7
Energy and power
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
12
Work done = force x distance moved, in joules. Power = work done / time, in watts.
Kinetic energy (energy of movement) = half x mass x velocity squared. Potential energy (energy of height) = mass x g x height, where g is 9.81 m/s squared.
Energy is conserved: it changes form but isn't lost, although some becomes heat through friction. Momentum (mass x velocity) is conserved in collisions.
Power sources include mechanical, electrical and renewable (solar, hydro, wind, geothermal), plus fossil fuels and nuclear.
e.g.
EXAMPLE
Lifting a 50 kg load 2 m gains 50 x 9.81 x 2 = 981 J of potential energy. Doing it in 5 s takes about 196 W.

## Slide 13
ENGINEERING CORE · Core topics 5 and 7
Energy and power
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
13
Quantity | Formula
Work done | Force x distance moved (J)
Power | Work done / time (W)
Kinetic energy | Half x mass x velocity squared
Potential energy | Mass x g x height (g = 9.81 m/s squared)
Momentum | Mass x velocity; conserved in collisions
Power sources: mechanical, electrical and renewable, e.g. solar, hydro, wind, geothermal, fossil fuels, nuclear.

## Slide 14
ENGINEERING CORE · Core topics 5 and 7
Quick check: Energy and power
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
14
1
What is the kinetic energy of 2 kg moving at 4 m/s?
2
A motor does 1,200 J in 20 s. What is its power?
3
What is the formula for potential energy?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. 16 J.
2. 60 W.
3. mgh.

## Slide 15
ENGINEERING CORE · Core topics 5 and 7
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
15
1
A 20 N force acts 0.5 m from a pivot. What is the moment?
2
What force accelerates a 2 kg mass at 3 m/s squared?
3
State Newton's third law.
4
What is the kinetic energy of 4 kg moving at 3 m/s?
5
A motor does 600 J of work in 10 s. What is its power?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 16
ENGINEERING CORE · Core topics 5 and 7
Answers
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
16
1
A 20 N force acts 0.5 m from a pivot. What is the moment?
10 N m.
2
What force accelerates a 2 kg mass at 3 m/s squared?
6 N.
3
State Newton's third law.
Every action has an equal and opposite reaction.
4
What is the kinetic energy of 4 kg moving at 3 m/s?
18 J.
5
A motor does 600 J of work in 10 s. What is its power?
60 W.
Notes: Talk through any answers the class found difficult.

## Slide 17
ENGINEERING CORE · Core topics 5 and 7
Activity: Beam challenge
Design and Development for Engineering and Manufacturing T Level · Forces, Motion and Energy
17
30 minutes
Pairs
1
A 6 m beam carries 2 kN at 2 m from the left support.
2
Calculate both support reactions.
3
Sketch the shear force diagram.
4
Check your reactions add up to the load.
SUCCESS CRITERIA
Moments taken correctly
Reactions of 1.33 kN (left) and 0.67 kN (right)
Diagram labelled
Notes: Answer: taking moments about the left support, right reaction = 2 x 2 / 6 = 0.67 kN; left reaction = 1.33 kN.

## Slide 18
ENGINEERING CORE · Core topics 5 and 7
Exit ticket
1
Give an everyday example of Newton's first law.
2
Why does a flywheel store energy?
3
Compare two power sources for a remote farm.
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 1
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/01-engineering-core-part1.md
Notes: Students answer on a sticky note or in the chat before leaving.