## Slide 1
ENGINEERING CORE
Fluid Dynamics and Thermodynamics
Core topic 5
Specification reference: 5.7, 5.8
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topic 5
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
2
By the end of this lesson you should be able to:
1
Explain hydrostatic pressure, viscosity and Bernoulli's principle.
2
Describe laminar and turbulent flow and aerodynamic forces.
3
Describe heat transfer and sensible and latent heat.
4
Apply Boyle's law, Charles' law and the general gas equation.
STARTER
Why do your ears hurt at the bottom of a swimming pool but not at the top?

## Slide 3
ENGINEERING CORE · Core topic 5
Fluids at rest and in motion
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
3
Hydrostatic pressure increases with depth: pressure = density x g x depth. That's why dams are thicker at the bottom.
Viscosity is a fluid's resistance to flowing: oil is more viscous than water.
Bernoulli's principle says that where a fluid speeds up, its pressure drops. It explains how carburettors and aircraft wings work.
Flow can be laminar (smooth, orderly layers) or turbulent (chaotic, swirling). Turbulence, vortices and separation points, where flow leaves a surface, increase drag.
e.g.
EXAMPLE
At 10 m depth in water, extra pressure = 1,000 x 9.81 x 10 = 98,100 Pa, nearly one extra atmosphere.

## Slide 4
ENGINEERING CORE · Core topic 5
Fluids at rest and in motion
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
4
1
Hydrostatic pressure
Pressure = density x g x depth. It rises with depth.
2
Viscosity
A fluid's resistance to flow: honey is more viscous than water.
3
Bernoulli's principle
Where a fluid speeds up, its pressure drops.
4
Flow types
Laminar (smooth layers) and turbulent (chaotic), with vortices and separation points.

## Slide 5
ENGINEERING CORE · Core topic 5
Quick check: Fluids at rest and in motion
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
5
1
What happens to pressure with depth?
2
State Bernoulli's principle.
3
What is viscosity?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. It increases.
2. Where a fluid speeds up, its pressure drops.
3. A fluid's resistance to flow.

## Slide 6
ENGINEERING CORE · Core topic 5
Aerodynamics
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
6
1
Lift
Upward force from pressure difference across a wing.
2
Drag
Resistance opposing motion through air.
3
Thrust
Force that drives an object forward.
Notes: Liquids are nearly incompressible; air is compressible, which is a key difference between liquid flow and aerodynamics.

## Slide 7
ENGINEERING CORE · Core topic 5
Heat
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
7
Heat moves by conduction (through solids, particle to particle), convection (by moving fluids, such as warm air rising) and radiation (by electromagnetic waves, needing no medium).
Sensible heat changes an object's temperature. Latent heat changes its state, such as ice melting, without changing temperature.
Materials expand when heated (expansivity), so engineers leave gaps in bridges and rails.
Systems are closed (no mass enters or leaves) or open (mass flows through, like an engine).
e.g.
EXAMPLE
A heatsink uses conduction to draw heat from a chip, then convection (a fan) to carry it away into the air.

## Slide 8
ENGINEERING CORE · Core topic 5
Heat
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
8
Heat transfer
Conduction: through solids
Convection: by moving fluids
Radiation: by electromagnetic waves
Open and closed systems
Types of heat
Sensible heat changes temperature
Latent heat changes state at constant temperature
Expansivity: materials expand when heated

## Slide 9
ENGINEERING CORE · Core topic 5
Quick check: Heat
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
9
1
Which heat transfer needs no medium?
2
What does latent heat do?
3
Why do bridges have expansion gaps?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Radiation.
2. Changes state without changing temperature.
3. Materials expand when heated.

## Slide 10
ENGINEERING CORE · Core topic 5
The gas laws
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
10
The gas laws link the pressure (p), volume (V) and temperature (T) of a gas. Temperature must be in kelvin: K = degrees C + 273.
Boyle's law, at constant temperature: p1 V1 = p2 V2. Squash a gas and its pressure rises.
Charles' law, at constant pressure: V1 / T1 = V2 / T2. Heat a gas and it expands.
The general gas equation combines them: p1 V1 / T1 = p2 V2 / T2. The characteristic gas equation, pV = mRT, links them to the mass of gas and its gas constant R.
e.g.
EXAMPLE
A gas at 100 kPa and 4 litres is compressed to 1 litre at constant temperature: p2 = 100 x 4 / 1 = 400 kPa.

## Slide 11
ENGINEERING CORE · Core topic 5
The gas laws
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
11
Law | Relationship | Held constant
Boyle's law | p1 V1 = p2 V2 | Temperature
Charles' law | V1 / T1 = V2 / T2 | Pressure
General gas equation | p1 V1 / T1 = p2 V2 / T2 | Mass of gas
Characteristic gas equation | pV = mRT | R for the gas
Temperatures in gas laws must be in kelvin: K = degrees C + 273.

## Slide 12
ENGINEERING CORE · Core topic 5
Quick check: The gas laws
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
12
1
What units must temperature be in?
2
Which law applies at constant temperature?
3
Convert 50 degrees C to kelvin.
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Kelvin.
2. Boyle's law.
3. 323 K.

## Slide 13
ENGINEERING CORE · Core topic 5
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
13
1
What happens to pressure as depth increases?
2
State Bernoulli's principle.
3
Which heat changes state without changing temperature?
4
A gas at 100 kPa is squeezed from 2 L to 1 L at constant temperature. New pressure?
5
Convert 27 degrees C to kelvin.
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 14
ENGINEERING CORE · Core topic 5
Answers
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
14
1
What happens to pressure as depth increases?
It increases.
2
State Bernoulli's principle.
Where a fluid's speed increases, its pressure decreases.
3
Which heat changes state without changing temperature?
Latent heat.
4
A gas at 100 kPa is squeezed from 2 L to 1 L at constant temperature. New pressure?
200 kPa.
5
Convert 27 degrees C to kelvin.
300 K.
Notes: Talk through any answers the class found difficult.

## Slide 15
ENGINEERING CORE · Core topic 5
Activity: Gas law problems
Design and Development for Engineering and Manufacturing T Level · Fluid Dynamics and Thermodynamics
15
25 minutes
Pairs
1
Solve the four gas law problems from your teacher.
2
State which law applies and what is held constant.
3
Convert all temperatures to kelvin.
4
Explain one real engineering application of each law.
SUCCESS CRITERIA
Correct law chosen
Kelvin used
Answers with units

## Slide 16
ENGINEERING CORE · Core topic 5
Exit ticket
1
Why must gas law temperatures be in kelvin?
2
Give one example of convection in engineering.
3
Why does a car spoiler create downforce?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 1
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/01-engineering-core-part1.md
Notes: Students answer on a sticky note or in the chat before leaving.