## Slide 1
ENGINEERING CORE
Materials: Chemistry, Properties and Structures
Core topics 5 and 6
Specification reference: 5.5, 6.1, 6.2
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topics 5 and 6
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
2
By the end of this lesson you should be able to:
1
Describe atomic structure, bonding and chemical behaviour of materials.
2
Distinguish physical and mechanical properties and calculate density.
3
Describe the main families of engineering materials.
4
Describe smart materials and their uses.
STARTER
Why is a kettle's body made of metal or plastic, but its handle always plastic?

## Slide 3
ENGINEERING CORE · Core topics 5 and 6
Chemistry for engineers
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
3
Atoms have a nucleus of protons and neutrons, surrounded by electrons. The outer (valence) electrons form bonds, which give materials their properties.
Metallic bonds share a 'sea' of electrons, making metals conduct and bend. Covalent bonds share electrons between atoms, giving strong, often brittle materials. Ionic bonds transfer electrons between atoms. Weak van der Waals forces hold polymer chains together.
Chemistry also matters for cells and batteries, electrolysis (used in plating) and how metals react with acids and alkalis, which is used in etching and surface finishing.
e.g.
EXAMPLE
Copper conducts electricity well because its metallic bonding lets electrons move freely.

## Slide 4
ENGINEERING CORE · Core topics 5 and 6
Chemistry for engineers
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
4
1
Atoms
Nucleus of protons and neutrons, surrounded by electrons; valence electrons form bonds.
2
Bonding
Metallic, covalent, ionic and van der Waals bonds.
3
Electrical chemistry
Cells, capacity, internal resistance and electrolysis.
4
Reactions
Metals react with acids and alkalis: used in etching and surface finishing.

## Slide 5
ENGINEERING CORE · Core topics 5 and 6
Quick check: Chemistry for engineers
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
5
1
Which particles form bonds?
2
Why do metals conduct electricity?
3
What is electrolysis used for in engineering?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Valence (outer) electrons.
2. Metallic bonding lets electrons move freely.
3. E.g. electroplating.

## Slide 6
ENGINEERING CORE · Core topics 5 and 6
Properties of materials
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
6
Physical properties describe how a material behaves without being loaded: density, melting point, thermal and electrical conductivity, expansivity, corrosion resistance, weldability and recyclability.
Mechanical properties describe how it responds to force. Strength resists breaking under tension, compression, shear or torsion. Hardness resists scratching and wear. Toughness absorbs impact without breaking; brittleness is the opposite. Ductility lets it be drawn into wire; malleability lets it be hammered into shape. Elasticity means it returns to shape; plasticity means it stays deformed.
Density = mass / volume.
e.g.
EXAMPLE
Glass is hard but brittle: it resists scratches but shatters on impact. Rubber is tough and elastic.

## Slide 7
ENGINEERING CORE · Core topics 5 and 6
Properties of materials
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
7
Physical
Density = mass / volume
Melting point
Thermal and electrical conductivity
Thermal expansivity, corrosion resistance
Weldability, recyclability
Mechanical
Strength: tensile, compressive, shear, torsion
Hardness and toughness
Brittleness and ductility
Elasticity and plasticity
Malleability

## Slide 8
ENGINEERING CORE · Core topics 5 and 6
Quick check: Properties of materials
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
8
1
What is the difference between hardness and toughness?
2
A 5.4 kg block is 0.002 cubic metres. What is its density?
3
What is ductility?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Hardness resists scratching; toughness resists breaking on impact.
2. 2,700 kg per cubic metre.
3. The ability to be drawn into wire.

## Slide 9
ENGINEERING CORE · Core topics 5 and 6
Families of materials
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
9
Ferrous metals contain iron, such as steels and cast iron. They're strong but most rust. Non-ferrous metals, such as aluminium, copper and brass, don't rust and are often lighter.
Thermoplastics, such as ABS and acrylic, soften when heated and can be reshaped and recycled. Thermosets, such as epoxy resin, set permanently when cured. Elastomers, such as rubber, stretch and return.
Composites combine materials: glass or carbon fibre in resin gives strength with low weight. Ceramics are hard and heat-resistant but brittle.
e.g.
EXAMPLE
A bike frame might be steel (ferrous, cheap), aluminium (non-ferrous, light) or carbon fibre composite (very light, expensive).

## Slide 10
ENGINEERING CORE · Core topics 5 and 6
Families of materials
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
10
Family | Examples
Ferrous metals | Cast iron, carbon steels, stainless steel
Non-ferrous metals | Aluminium, copper, brass, zinc
Thermoplastics / thermosets | ABS, acrylic / epoxy resin, melamine
Elastomers | Rubber, neoprene
Composites | GRP, carbon fibre (CRP), MDF
Ceramics | Silicon carbide, glass

## Slide 11
ENGINEERING CORE · Core topics 5 and 6
Quick check: Families of materials
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
11
1
What is a ferrous metal?
2
What is the difference between thermoplastics and thermosets?
3
Why use composites?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. One containing iron.
2. Thermoplastics can be reshaped when heated; thermosets set permanently.
3. High strength with low weight.

## Slide 12
ENGINEERING CORE · Core topics 5 and 6
Smart materials
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
12
1
Shape memory alloys
Return to a set shape when heated.
2
Quantum tunnelling composite
Conducts when squeezed.
3
Thermochromic / photochromic
Change colour with heat / light.
4
Piezoelectric crystals
Produce a voltage when stressed.

## Slide 13
ENGINEERING CORE · Core topics 5 and 6
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
13
1
A block has mass 2.7 kg and volume 0.001 cubic metres. What is its density?
2
What is the difference between hardness and toughness?
3
Is brass ferrous or non-ferrous?
4
Which smart material produces a voltage under stress?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 14
ENGINEERING CORE · Core topics 5 and 6
Answers
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
14
1
A block has mass 2.7 kg and volume 0.001 cubic metres. What is its density?
2,700 kg per cubic metre (aluminium).
2
What is the difference between hardness and toughness?
Hardness resists scratching and wear; toughness resists fracture from impact.
3
Is brass ferrous or non-ferrous?
Non-ferrous.
4
Which smart material produces a voltage under stress?
A piezoelectric crystal.
Notes: Talk through any answers the class found difficult.

## Slide 15
ENGINEERING CORE · Core topics 5 and 6
Activity: Material detective
Design and Development for Engineering and Manufacturing T Level · Materials: Chemistry, Properties and Structures
15
25 minutes
Small groups
1
Examine the material samples from your teacher.
2
Identify each family and one likely material.
3
Measure mass and volume to calculate density for two samples.
4
Match each sample to a suitable product and justify it by properties.
SUCCESS CRITERIA
Families correct
Density calculated with units
Justifications use property names

## Slide 16
ENGINEERING CORE · Core topics 5 and 6
Exit ticket
1
Why are thermosets used for plug sockets?
2
What is ductility?
3
Name one use of a shape memory alloy.
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 1
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/01-engineering-core-part1.md
Notes: Students answer on a sticky note or in the chat before leaving.