## Slide 1
ENGINEERING CORE
Material Processing, Treatment, Failure and Testing
Core topic 6
Specification reference: 6.3, 6.4, 6.5, 6.6
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topic 6
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
2
By the end of this lesson you should be able to:
1
Explain how processing changes material properties.
2
Describe heat treatments and surface treatments.
3
Explain causes of failure: corrosion, fatigue and creep.
4
Interpret tensile test results and calculate stress, strain and Young's modulus.
STARTER
Bend a paperclip back and forth until it snaps. What just happened to the metal?

## Slide 3
ENGINEERING CORE · Core topic 6
Heat and surface treatments
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
3
Heat treatments change a metal's structure and properties.
Quench hardening heats steel and cools it rapidly, making it very hard but brittle; tempering then reheats it gently to reduce brittleness. Case hardening gives a hard outer skin with a tough core. Annealing softens metal and relieves stress; normalising refines its grain. Precipitation hardening strengthens some alloys, such as aluminium.
Surface treatments protect against corrosion: painting and plastic coating form a barrier; galvanising coats steel with zinc, which corrodes first to protect it.
Processing, such as rolling, forging and welding, also changes properties.
e.g.
EXAMPLE
A chisel is quench hardened so its edge stays sharp, then tempered so it doesn't shatter when hit with a hammer.

## Slide 4
ENGINEERING CORE · Core topic 6
Heat and surface treatments
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
4
Treatment | Effect
Case hardening | Hard outer surface, tough core
Quench hardening / tempering | Harden steel, then reduce brittleness
Normalising / annealing | Refine grain / soften and relieve stress
Precipitation hardening | Strengthens some alloys, e.g. aluminium
Painting, plastic coating, galvanising | Barrier or sacrificial protection against corrosion
Notes: Processing also changes properties: rolling, forging, welding, casting, sintering, hot and cold working, curing thermosets.

## Slide 5
ENGINEERING CORE · Core topic 6
Quick check: Heat and surface treatments
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
5
1
Why temper after quench hardening?
2
What does annealing do?
3
How does galvanising protect steel?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. To reduce brittleness.
2. Softens the metal and relieves stress.
3. The zinc coating corrodes first.

## Slide 6
ENGINEERING CORE · Core topic 6
Why materials fail
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
6
Corrosion is chemical attack, such as rust, that removes material and can eventually perforate it. It includes oxidation, chemical attack and stress corrosion.
Fatigue is failure under repeated loading, even when each load is well below the breaking stress: tiny cracks grow with every cycle until the part snaps.
Creep is slow, permanent deformation under a constant load, especially at high temperature. It happens in three stages: primary, secondary (steady) and tertiary, ending in fracture.
Prevention includes coatings, galvanising, sacrificial anodes and designing out stress concentrations.
e.g.
EXAMPLE
Bending a paperclip back and forth until it snaps is fatigue: no single bend breaks it, but the repeated cycles do.

## Slide 7
ENGINEERING CORE · Core topic 6
Why materials fail
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
7
1
Corrosion
Oxidation, chemical attack or stress corrosion eats material away.
2
Fatigue
Repeated loading below the breaking stress causes cracks: the paperclip.
3
Creep
Slow deformation under constant load, often at high temperature, in three stages.
4
Prevention
Coatings, galvanising, sacrificial anodes, good design.

## Slide 8
ENGINEERING CORE · Core topic 6
Quick check: Why materials fail
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
8
1
What is fatigue?
2
When is creep a concern?
3
What is a sacrificial anode?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Failure from repeated loading below the breaking stress.
2. Under constant load, especially at high temperature.
3. A more reactive metal that corrodes instead of the protected part.

## Slide 9
ENGINEERING CORE · Core topic 6
Tensile testing
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
9
A tensile test stretches a sample until it breaks, recording the load and extension.
Stress = force / cross-sectional area. Strain = extension / original length (no units). In the elastic region, extension is proportional to load (Hooke's law) and the sample returns to shape. Young's modulus = stress / strain in this region, a measure of stiffness.
Beyond the elastic limit it deforms plastically. The ultimate tensile strength is the maximum stress; after that the sample narrows (necks) and fractures.
Other tests include hardness, impact (toughness), fatigue (Wohler), wear and corrosion.
e.g.
EXAMPLE
A 10 kN load on a 50 square millimetre bar gives a stress of 10,000 / 0.00005 = 200 MPa.

## Slide 10
ENGINEERING CORE · Core topic 6
Tensile testing
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
10
Quantity | Formula or meaning
Stress | Force / cross-sectional area (N per square metre, Pa)
Strain | Extension / original length (no units)
Young's modulus | Stress / strain, in the elastic region
Hooke's law | Extension is proportional to load up to the limit of proportionality
Ultimate tensile strength | The maximum stress before necking and fracture
Other tests: visual, toughness (impact), hardness, corrosion, wear, fatigue (Wohler), conductivity.

## Slide 11
ENGINEERING CORE · Core topic 6
Quick check: Tensile testing
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
11
1
What is the formula for stress?
2
What does Young's modulus measure?
3
What is necking?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Force / area.
2. Stiffness (stress / strain).
3. The sample narrowing before it fractures.

## Slide 12
ENGINEERING CORE · Core topic 6
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
12
1
What is fatigue failure?
2
A 1,000 N force acts on 0.0001 square metres. What is the stress?
3
A 2 m bar stretches 1 mm. What is the strain?
4
Why temper after quench hardening?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 13
ENGINEERING CORE · Core topic 6
Answers
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
13
1
What is fatigue failure?
Failure caused by repeated cyclic loading below the ultimate strength.
2
A 1,000 N force acts on 0.0001 square metres. What is the stress?
10,000,000 Pa (10 MPa).
3
A 2 m bar stretches 1 mm. What is the strain?
0.0005.
4
Why temper after quench hardening?
To reduce brittleness.
Notes: Talk through any answers the class found difficult.

## Slide 14
ENGINEERING CORE · Core topic 6
Activity: Read a load-extension graph
Design and Development for Engineering and Manufacturing T Level · Material Processing, Treatment, Failure and Testing
14
25 minutes
Pairs
1
Use the tensile test data from your teacher.
2
Mark the elastic limit, UTS and fracture point on the graph.
3
Calculate stress, strain and Young's modulus in the elastic region.
4
Identify the material from its modulus.
SUCCESS CRITERIA
Key points labelled
Calculations with units
Sensible identification

## Slide 15
ENGINEERING CORE · Core topic 6
Exit ticket
1
Why is galvanising called sacrificial protection?
2
Where would creep be a concern?
3
What does Young's modulus tell you?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 1
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/01-engineering-core-part1.md
Notes: Students answer on a sticky note or in the chat before leaving.