## Slide 1
ENGINEERING CORE
Continuous Improvement
Core topic 16
Specification reference: 16.1
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
ENGINEERING CORE · Core topic 16
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Continuous Improvement
2
By the end of this lesson you should be able to:
1
Explain the PDCA cycle, KPIs, lean and Kaizen.
2
Identify the 8 wastes.
3
Describe continuous improvement practices such as 6S, SMED, OEE and TPM.
STARTER
Watch a classmate make a cup of tea (or imagine it). How many unnecessary steps do they take?

## Slide 3
ENGINEERING CORE · Core topic 16
The PDCA cycle
Design and Development for Engineering and Manufacturing T Level · Continuous Improvement
3
Continuous improvement means making small, steady improvements all the time, known as Kaizen.
The PDCA cycle structures it. Plan: identify a problem and plan a change. Do: try it on a small scale. Check: measure the results against key performance indicators (KPIs). Act: adopt it if it worked, adjust it, or abandon it, then start again.
KPIs, such as scrap rate, output per hour or on-time delivery, show whether things are really improving. Lean thinking focuses on removing waste.
e.g.
EXAMPLE
Plan: rearrange a workbench to cut walking. Do: trial it for a week. Check: assembly time falls 12%. Act: roll it out to all benches.

## Slide 4
ENGINEERING CORE · Core topic 16
The PDCA cycle
Design and Development for Engineering and Manufacturing T Level · Continuous Improvement
4
1
Plan
Identify the problem and plan a change.
2
Do
Try it on a small scale.
3
Check
Measure results against KPIs.
4
Act
Adopt, adjust or abandon, then repeat.
Kaizen means small, continuous, incremental improvements by everyone.

## Slide 5
ENGINEERING CORE · Core topic 16
Quick check: The PDCA cycle
Design and Development for Engineering and Manufacturing T Level · Continuous Improvement
5
1
What does PDCA stand for?
2
What is Kaizen?
3
Why use KPIs?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Plan, do, check, act.
2. Continuous small improvements by everyone.
3. To measure whether changes really improve things.

## Slide 6
ENGINEERING CORE · Core topic 16
The 8 wastes
Design and Development for Engineering and Manufacturing T Level · Continuous Improvement
6
Lean identifies eight wastes that add cost but no value.
Transportation: moving materials unnecessarily. Inventory: holding too much stock. Motion: people moving more than needed. Waiting: idle time. Over-production: making more than is needed. Over-processing: doing more work than the customer requires. Defects: scrap and rework. Unused talent: not using people's skills and ideas.
Practices such as value stream mapping, 6S, SMED, OEE, TPM and kanban help remove them.
e.g.
EXAMPLE
Polishing a hidden internal surface the customer never sees is over-processing: it costs time and adds no value.

## Slide 7
ENGINEERING CORE · Core topic 16
The 8 wastes
Design and Development for Engineering and Manufacturing T Level · Continuous Improvement
7
1
Transportation
Moving materials unnecessarily.
2
Inventory
Too much stock.
3
Motion
People moving more than needed.
4
Waiting
Idle time.
5
Over-production and over-processing
Making too much, or doing more than required.
6
Defects and unused talent
Scrap and rework; not using people's skills.

## Slide 8
ENGINEERING CORE · Core topic 16
Quick check: The 8 wastes
Design and Development for Engineering and Manufacturing T Level · Continuous Improvement
8
1
Name four of the 8 wastes.
2
What is over-processing?
3
Why is unused talent a waste?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Any four of the eight.
2. Doing more than the customer requires.
3. People's skills and ideas aren't being used.

## Slide 9
ENGINEERING CORE · Core topic 16
Improvement practices
Design and Development for Engineering and Manufacturing T Level · Continuous Improvement
9
Value stream mapping draws every step of a process to find waste. Visual management and kanban make status and demand visible at a glance.
6S organises the workplace: sort, set in order, shine, standardise, sustain and safety.
SMED (single minute exchange of dies) cuts changeover times so small batches become practical.
OEE (overall equipment effectiveness) = availability x performance x quality, showing how well a machine is really used. TPM (total productive maintenance) has operators help maintain their own machines.
e.g.
EXAMPLE
A press is available 90% of the time, runs at 80% speed and makes 95% good parts: OEE = 0.9 x 0.8 x 0.95 = about 68%.

## Slide 10
ENGINEERING CORE · Core topic 16
Improvement practices
Design and Development for Engineering and Manufacturing T Level · Continuous Improvement
10
Practice | Purpose
Value stream mapping | Map every step to find waste
Visual management and kanban | Make status and demand visible at a glance
6S | Sort, set in order, shine, standardise, sustain, safety
SMED | Single minute exchange of dies: faster changeovers
OEE | Overall equipment effectiveness = availability x performance x quality
TPM | Total productive maintenance: operators help maintain machines

## Slide 11
ENGINEERING CORE · Core topic 16
Quick check: Improvement practices
Design and Development for Engineering and Manufacturing T Level · Continuous Improvement
11
1
What is the OEE formula?
2
What does SMED reduce?
3
Name the six parts of 6S.
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Availability x performance x quality.
2. Changeover time.
3. Sort, set in order, shine, standardise, sustain, safety.

## Slide 12
ENGINEERING CORE · Core topic 16
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Continuous Improvement
12
1
What does PDCA stand for?
2
Name four of the 8 wastes.
3
What does SMED reduce?
4
A machine is 90% available, 80% performance and 95% quality. OEE?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 13
ENGINEERING CORE · Core topic 16
Answers
Design and Development for Engineering and Manufacturing T Level · Continuous Improvement
13
1
What does PDCA stand for?
Plan, do, check, act.
2
Name four of the 8 wastes.
Any four, e.g. transportation, inventory, motion, waiting.
3
What does SMED reduce?
Changeover time.
4
A machine is 90% available, 80% performance and 95% quality. OEE?
About 68%.
Notes: Talk through any answers the class found difficult.

## Slide 14
ENGINEERING CORE · Core topic 16
Activity: Lean the process
Design and Development for Engineering and Manufacturing T Level · Continuous Improvement
14
30 minutes
Small groups
1
Map the value stream of a simple workshop task.
2
Mark every waste using the 8 wastes.
3
Apply 6S to the work area.
4
Plan one PDCA cycle to test an improvement.
SUCCESS CRITERIA
At least five wastes identified
6S steps applied
PDCA plan has a measurable KPI

## Slide 15
ENGINEERING CORE · Core topic 16
Exit ticket
1
Which waste is most common in your workshop?
2
Why use KPIs in continuous improvement?
3
What is the difference between Kaizen and a big one-off change?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Engineering Core, Part 2
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/01-core-component/02-engineering-core-part2.md
Notes: Students answer on a sticky note or in the chat before leaving.