## Slide 1
MECHANICAL ENGINEERING
Mechanical Drawings, Standards and Communication
Mechanical: Knowledge criteria
Specification reference: 1.3, 1.4, 1.20
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Mechanical Drawings, Standards and Communication
2
By the end of this lesson you should be able to:
1
Interpret orthographic drawings, sections and standard features.
2
Explain the role of BSI, ISO and IMechE.
3
Choose methods and formats to communicate engineering information.
4
Explain CAD to CAM transfer and the uses of 2D, 3D and CAE tools.
STARTER
How would you explain the design of a gear to a machinist, a customer and a manager? Would you use the same drawing?

## Slide 3
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Mechanical drawings
Design and Development for Engineering and Manufacturing T Level · Mechanical Drawings, Standards and Communication
3
Orthographic drawings show accurate views on standard sheet sizes. Section views show the inside of a part as if cut through, with the cut surfaces hatched.
Standard features such as springs, splines, gears, webs, solid shafts, keys and keyways are drawn using simplified conventions, so they don't need drawing in full detail.
Symbols such as balloons (numbering parts on an assembly), diameter and depth follow BS EN 8888, so any engineer can read the drawing the same way.
e.g.
EXAMPLE
A gearbox assembly drawing uses balloons to number each part, matching a parts list, and a section view shows the bearings inside.

## Slide 4
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Mechanical drawings
Design and Development for Engineering and Manufacturing T Level · Mechanical Drawings, Standards and Communication
4
1
Orthographic drawings
Sheet sizes, views, section views and hatching.
2
Standard features
Springs, splines, gears, webs, solid shafts, keys and keyways.
3
Symbols
Balloons, diameter, depth, per BS EN 8888.

## Slide 5
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Quick check: Mechanical drawings
Design and Development for Engineering and Manufacturing T Level · Mechanical Drawings, Standards and Communication
5
1
What does a section view show?
2
What is a balloon on a drawing?
3
Which standard covers drawing conventions?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. The inside of a part as if cut through.
2. A numbered label identifying a part.
3. BS EN 8888.

## Slide 6
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Standards bodies
Design and Development for Engineering and Manufacturing T Level · Mechanical Drawings, Standards and Communication
6
1
BSI
British Standards Institution: UK standards.
2
ISO
International Organization for Standardization.
3
IMechE
Institution of Mechanical Engineers: professional codes and guidance.
Notes: Learners should know how to access and interpret regulatory requirements for mechanical component design.

## Slide 7
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Communicating engineering information
Design and Development for Engineering and Manufacturing T Level · Mechanical Drawings, Standards and Communication
7
Engineering information is shared as CAD models and drawings, written specifications, SOPs and reports, presentations, graphs of test data and SPC, and CNC programs sent to machines.
The audience decides the format: designers and manufacturing engineers need precise drawings and data; customers need clear visuals; non-technical staff need plain summaries.
Digital tools help: 2D CAD for manufacturing drawings, 3D CAD for models and assemblies, CAE to simulate performance, and CAD to CAM transfer to send toolpaths to CNC machines.
e.g.
EXAMPLE
The same bracket: a toleranced drawing for the machinist, a rendered 3D image for the customer, and a one-paragraph cost summary for the manager.

## Slide 8
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Communicating engineering information
Design and Development for Engineering and Manufacturing T Level · Mechanical Drawings, Standards and Communication
8
Methods
CAD models and engineering drawings
Specifications, SOPs and reports
Presentations
Graphs of performance data and SPC
Sending programs to CNC machines
Audiences
Designers
Manufacturing engineers
Customers
Non-technical personnel

## Slide 9
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Quick check: Communicating engineering information
Design and Development for Engineering and Manufacturing T Level · Mechanical Drawings, Standards and Communication
9
1
What does CAE do?
2
How do CNC machines get instructions from CAD?
3
Why adapt the format to the audience?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Simulates how a design will perform.
2. Through CAD to CAM transfer.
3. Each audience needs different detail and language.

## Slide 10
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Digital tools
Design and Development for Engineering and Manufacturing T Level · Mechanical Drawings, Standards and Communication
10
1
2D CAD
Fast, clear drawings for manufacture.
2
3D CAD
Solid models, assemblies and clash checks.
3
CAD to CAM
Toolpaths sent by direct entry, intranet or Wi-Fi to CNC machines.
4
CAE and visualisation
Simulate assembly performance; render for customers.

## Slide 11
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Mechanical Drawings, Standards and Communication
11
1
Which standard covers technical drawings?
2
What does a section view show?
3
What is CAE used for?
4
Who is IMechE?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 12
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Answers
Design and Development for Engineering and Manufacturing T Level · Mechanical Drawings, Standards and Communication
12
1
Which standard covers technical drawings?
BS EN 8888.
2
What does a section view show?
The inside of a part as if cut through, with hatching.
3
What is CAE used for?
Simulating and analysing how a design will perform.
4
Who is IMechE?
The Institution of Mechanical Engineers.
Notes: Talk through any answers the class found difficult.

## Slide 13
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Activity: Three audiences
Design and Development for Engineering and Manufacturing T Level · Mechanical Drawings, Standards and Communication
13
30 minutes
Small groups
1
Take a simple component such as a shaft with a keyway.
2
Produce a detailed drawing for the machinist.
3
Produce a visual for the customer.
4
Write a one-paragraph summary for a manager.
SUCCESS CRITERIA
Drawing follows BS EN 8888
Customer visual has no jargon
Summary is concise

## Slide 14
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Exit ticket
1
When is 2D CAD better than 3D?
2
What is a keyway for?
3
How does data get from CAD to a CNC machine?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Knowledge Criteria
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/02-occupational-specialism/01-knowledge-criteria.md
Notes: Students answer on a sticky note or in the chat before leaving.