## Slide 1
MECHANICAL ENGINEERING
Simple Machines and Mechanical Calculations
Mechanical: Knowledge criteria
Specification reference: 1.5, 1.6, 1.13
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
2
By the end of this lesson you should be able to:
1
Describe gears, pulleys, levers, linkages, cams and ratchets.
2
Calculate gear ratios for simple and compound gear trains.
3
Calculate mechanical advantage, velocity ratio and efficiency.
4
Apply stress, strain and beam calculations to design.
STARTER
A bike's pedal gear has 48 teeth and the rear gear has 16. How many times does the wheel turn for each pedal turn?

## Slide 3
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Simple machines
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
3
Simple machines change the size, direction or type of motion.
Gears transmit rotation: spur gears (parallel shafts), helical (quieter), bevel (turning through 90 degrees), worm (large reductions) and rack and pinion (rotary to linear).
Levers are class 1 (pivot in the middle, like a seesaw), class 2 (load in the middle, like a wheelbarrow) or class 3 (effort in the middle, like tweezers).
Linkages include reverse motion, parallel motion, bell crank and crank and slider. Cams (circular, eccentric, snail) turn rotation into reciprocating motion. Pulleys change the direction of force and ratchets allow movement one way only.
e.g.
EXAMPLE
A car's steering uses a rack and pinion to turn the steering wheel's rotation into the sideways motion that turns the wheels.

## Slide 4
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Simple machines
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
4
1
Gears
Spur, helical, bevel, worm, rack and pinion.
2
Levers
Class 1 (seesaw), class 2 (wheelbarrow), class 3 (tweezers).
3
Linkages
Reverse motion, parallel motion, bell crank, crank and slider.
4
Cams
Circular, eccentric and snail (drop) cams turn rotary into reciprocating motion.
5
Pulleys and ratchets
Change force direction; allow motion one way only.
Notes: Each machine changes the magnitude, direction or type of motion.

## Slide 5
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Quick check: Simple machines
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
5
1
Which gear turns rotation into linear motion?
2
Which lever class is a wheelbarrow?
3
What does a cam do?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Rack and pinion.
2. Class 2.
3. Turns rotary motion into reciprocating motion.

## Slide 6
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Gear trains
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
6
Gear ratio = teeth on the driven gear / teeth on the driver gear.
Output speed = input speed / gear ratio. A ratio above 1 slows the output but increases torque; below 1 speeds it up and reduces torque.
In a compound gear train, two gears share a shaft. Multiply the ratios of each pair to get the overall ratio, which allows large reductions in a small space.
An idler gear between two gears changes the direction of rotation but not the ratio.
e.g.
EXAMPLE
Driver 20 teeth to driven 60 teeth (3:1), then on the same shaft 15 teeth to 45 teeth (3:1). Overall ratio = 3 x 3 = 9:1, so 900 rpm in gives 100 rpm out.

## Slide 7
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Gear trains
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
7
Gear ratio = teeth on driven gear / teeth on driver gear.
Output speed = input speed / gear ratio.
Compound train: multiply the ratios of each pair.
Starter: 16 / 48 = 1/3, so the wheel turns 3 times per pedal turn.
!
KEY IDEA
A ratio above 1 slows the output and increases torque. Below 1 speeds it up and reduces torque.

## Slide 8
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Quick check: Gear trains
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
8
1
A 25-tooth driver meshes with a 75-tooth gear. Gear ratio?
2
If the input is 1,200 rpm through a 4:1 ratio, what is the output?
3
How do you find a compound train's ratio?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. 3:1.
2. 300 rpm.
3. Multiply the ratios of each pair.

## Slide 9
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Machine performance
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
9
Mechanical advantage (MA) = load / effort. It shows how much a machine multiplies force.
Velocity ratio (VR) = distance moved by the effort / distance moved by the load. It depends only on the machine's geometry.
Efficiency = MA / VR x 100%. Real machines are never 100% efficient because of friction and the weight of moving parts.
Work = force x distance, and power = work / time.
e.g.
EXAMPLE
A pulley system lifts 800 N with 250 N effort. The effort moves 4 m while the load rises 1 m. MA = 3.2, VR = 4, efficiency = 80%.

## Slide 10
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Machine performance
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
10
Quantity | Formula
Mechanical advantage (MA) | Load / effort
Velocity ratio (VR) | Distance moved by effort / distance moved by load
Efficiency | MA / VR x 100%
Work | Force x distance
Power | Work / time

## Slide 11
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Quick check: Machine performance
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
11
1
What is the formula for mechanical advantage?
2
If MA is 3 and VR is 4, what is the efficiency?
3
Why is efficiency never 100%?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Load / effort.
2. 75%.
3. Friction and the weight of moving parts.

## Slide 12
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Force calculations
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
12
Quantity | Formula
Stress | Force / area
Strain | Extension / original length
Young's modulus | Stress / strain
Beam reactions | Take moments about a support; reactions sum to the total load
Material quantity and cost | Area or volume x unit cost, plus manufacturing cost
Notes: Beams can be simply supported or cantilevered; learners calculate reactions, shear force and bending moment.

## Slide 13
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
13
1
A 20-tooth driver meshes with a 60-tooth driven gear. Gear ratio?
2
If the driver turns at 900 rpm, what is the output speed?
3
A pulley lifts 400 N with 100 N effort. MA?
4
If VR is 5 and MA is 4, what is the efficiency?
5
Which lever class is a wheelbarrow?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 14
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Answers
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
14
1
A 20-tooth driver meshes with a 60-tooth driven gear. Gear ratio?
3:1.
2
If the driver turns at 900 rpm, what is the output speed?
300 rpm.
3
A pulley lifts 400 N with 100 N effort. MA?
4.
4
If VR is 5 and MA is 4, what is the efficiency?
80%.
5
Which lever class is a wheelbarrow?
Class 2.
Notes: Talk through any answers the class found difficult.

## Slide 15
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Activity: Design a winch
Design and Development for Engineering and Manufacturing T Level · Simple Machines and Mechanical Calculations
15
35 minutes
Pairs
1
A winch must lift 2,000 N using a 250 N effort.
2
Design a compound gear train to achieve it.
3
Calculate MA, VR and efficiency assuming 80% efficiency.
4
Suggest where a ratchet is needed and why.
SUCCESS CRITERIA
Gear ratio calculated correctly
Efficiency accounted for
Ratchet placement justified

## Slide 16
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Exit ticket
1
Why can't efficiency ever reach 100%?
2
Which gear type changes the axis by 90 degrees?
3
What does a cam follower do?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Knowledge Criteria
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/02-occupational-specialism/01-knowledge-criteria.md
Notes: Students answer on a sticky note or in the chat before leaving.