## Slide 1
MECHANICAL ENGINEERING
Quality, Testing and Measurement
Mechanical: Knowledge criteria
Specification reference: 1.15, 1.17, 1.18, 1.19
Design and Development for Engineering and Manufacturing T Level · Lesson slides
Unofficial teaching resource. Check the official City & Guilds specification for assessment detail.

## Slide 2
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Learning objectives
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
2
By the end of this lesson you should be able to:
1
Distinguish assignable from random causes of error.
2
Compare quality assurance and quality control, and sampling with 100% inspection.
3
Compare non-destructive and destructive testing methods.
4
Choose measurement equipment and analyse measurement data statistically.
STARTER
Two operators measure the same part and get different results. List every reason why.

## Slide 3
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Causes of error
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
3
Assignable (systematic) causes have an identifiable reason: faulty calibration, tool wear, observer bias or human error. They push results consistently one way and can be found and fixed.
Random causes come from ambient conditions such as temperature and humidity, and instrument uncertainty. They scatter results unpredictably and can be reduced but never eliminated.
Quality assurance prevents errors through procedures, calibration, process capability monitoring and preventative maintenance. Quality control catches them through testing and inspection. High volumes suit sampling; critical or low-volume parts may need 100% inspection.
e.g.
EXAMPLE
Every shaft measures 0.05 mm oversize: a systematic error, probably worn tooling or a misset machine. Readings scattered either side point to random error.

## Slide 4
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Causes of error
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
4
Assignable (systematic)
Faulty calibration
Tool wear
Observer bias
Human error
Can be found and fixed
Random
Ambient conditions
Temperature and humidity
Instrument uncertainty
Reduced, not eliminated
Notes: Quality assurance: procedures, calibration, process capability monitoring, preventative maintenance. Quality control: testing and inspection. Production quantity decides between sampling and 100% inspection.

## Slide 5
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Quick check: Causes of error
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
5
1
Is tool wear an assignable or random cause?
2
Can random error be eliminated?
3
When is 100% inspection used?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Assignable.
2. No, only reduced.
3. For critical or low-volume parts.

## Slide 6
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Testing methods
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
6
Non-destructive testing (NDT) checks parts without damaging them. Visual inspection, measurement and go/no-go gauges find surface and size faults. Penetrant testing and magnetic particle inspection reveal surface cracks. Ultrasonic testing and X-radiography find flaws inside.
Destructive testing sacrifices a sample: tensile tests (strength), hardness tests, impact tests such as Izod and Charpy (toughness) and macro examination (internal structure).
NDT can check every part; destructive tests check samples from a batch.
e.g.
EXAMPLE
Every weld on a pressure vessel is X-rayed (NDT), while sample welds from the same batch are cut and tensile tested (destructive).

## Slide 7
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Testing methods
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
7
Type | Method | Detects
Non-destructive | Visual, measurement, go/no-go gauges | Surface and dimensional faults
Non-destructive | Ultrasonic, X-radiography | Internal flaws
Non-destructive | Penetrant, magnetic particle | Surface cracks
Destructive | Tensile, hardness | Strength and hardness
Destructive | Impact (Izod, Charpy), macro examination | Toughness and internal structure

## Slide 8
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Quick check: Testing methods
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
8
1
Which NDT method finds internal flaws?
2
What does a Charpy test measure?
3
Why can't destructive testing check every part?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Ultrasonic or X-radiography.
2. Toughness (impact energy absorbed).
3. The part is destroyed.

## Slide 9
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Measurement equipment
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
9
Choose equipment by what's being measured and how accurately.
Rules and protractors for basic length and angle. Vernier and digital callipers for inside, outside and depth. Micrometers for precise small dimensions. Gauges: go/no-go for quick pass or fail, slip gauges as precise reference lengths, plug gauges for holes. Dial test indicators for run-out. CMMs and laser scanning for complex 3D shapes. Digital stress and strain machines for mechanical properties.
Analyse readings statistically: mean, range and standard deviation show whether a process is in tolerance.
e.g.
EXAMPLE
Ten shafts measure 20.01, 20.02, 20.00... The mean of 20.01 mm and a small standard deviation show the process is centred and consistent.

## Slide 10
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Measurement equipment
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
10
Equipment | Use
Rules, protractors | Basic length and angle
Vernier and digital callipers | Inside, outside and depth
Micrometers (outside, inside, depth) | Precise small dimensions
Gauges (go/no-go, slip, plug) | Quick pass or fail checks; reference lengths
DTI, CMM, laser scanning | Run-out, complex 3D geometry
Digital stress/strain machines | Mechanical properties
Analyse results with mean, range and standard deviation to judge whether parts are in tolerance.

## Slide 11
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Quick check: Measurement equipment
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
11
1
What is a go/no-go gauge for?
2
What is a slip gauge?
3
What does a large standard deviation show?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. A quick pass or fail check.
2. A precise reference length.
3. Readings vary a lot, so the process is inconsistent.

## Slide 12
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Check your understanding
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
12
1
Is tool wear an assignable or random cause?
2
Which test finds internal flaws without damaging the part?
3
What does a Charpy test measure?
4
What does a go/no-go gauge do?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 13
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Answers
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
13
1
Is tool wear an assignable or random cause?
Assignable.
2
Which test finds internal flaws without damaging the part?
Ultrasonic testing or X-radiography.
3
What does a Charpy test measure?
Toughness (impact energy absorbed).
4
What does a go/no-go gauge do?
Quickly checks whether a feature is within limits.
Notes: Talk through any answers the class found difficult.

## Slide 14
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Activity: Is the batch in tolerance?
Design and Development for Engineering and Manufacturing T Level · Quality, Testing and Measurement
14
30 minutes
Pairs, practical
1
Measure ten parts with a micrometer.
2
Calculate the mean, range and standard deviation.
3
Compare with the drawing tolerance.
4
Decide whether the process needs adjusting and suggest a cause.
SUCCESS CRITERIA
Measurements recorded correctly
Statistics accurate
Decision justified

## Slide 15
MECHANICAL ENGINEERING · Mechanical: Knowledge criteria
Exit ticket
1
When would you use destructive testing?
2
Why calibrate measuring equipment?
3
What does a large standard deviation tell you?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Knowledge Criteria
https://lana6478.github.io/T-level-Design-Development-Engineering-Manufacturing/#/02-occupational-specialism/01-knowledge-criteria.md
Notes: Students answer on a sticky note or in the chat before leaving.